## Slide 1
Jockey Club
STEAM Education Resources Sharing Scheme
Unit 1-
DIY a Thermocycler
To be a Food Detective

## Slide 2: Aims of Unit 1
Build a thermocycler
Evaluate the function of the thermocycler
Building Thermocycler
DNA Extraction and Gel Electrophoresis
PCR and Gel Electrophoresis
RFLP and DNA Fingerprinting

## Slide 3: Objectives of Unit 1
Utilise design tools, materials, and information
Understand the basic principles of electronic systems and various forms of system and control
Use programmable control boards and kits
Interpret truth tables for simple logic gates
Construct simple programmable control systems to solve control problems
Analyse and evaluate manufactured products

## Slide 4: Content
What is a Thermocycler?
Structure and Working Mechanism of a DIY Thermocycler
Hands-on activity -- Building a DIY Thermocycler

## Slide 5
What is a Thermocycler

## Slide 6: Thermocycler is an Instrument for PCR
PCR stands for Polymerase Chain Reaction
It is a common technique for
  Gene detection
  Gene amplification

## Slide 7: PCR Involves Multiple Temperature Changes

## Slide 8: PCR Involves Multiple Temperature Changes

## Slide 9: A Thermocycler is Used to Control Reaction Temperature
Image credits: Left: Photo by Madprime is licensed under CC0 1.0 Universal Public Domain Dedication Right: G-STORM GS4 thermal cycler by Rror is licensed under CC BY-SA 3.0

## Slide 10: The “Ancient” Thermocycler

## Slide 11: A Lightbulb Thermocycler

## Slide 12
Structure and Working Mechanism of a DIY Thermocycler

## Slide 13: Structure of a Lightbulb Thermocycler

## Slide 14: Working Principle of a Thermocycler
Thermistor senses the temperature
Signal is sent to the control board
Control board maintain desired temperature for desired duration

## Slide 15: Working Principle of a Thermocycler
Heating
Cooling

## Slide 16: Electric Circuits for Control
Heating Circuit
Cooling Circuit
Probing Circuit
Signaling Circuit
Image credit: “Electronic Circuit” by Nicola Asuni is licensed under CC BY-SA 3.0

## Slide 17: Electric Circuits for Control
Heating Circuit
  200W incandescent bulb
  Relay
  Powered by 220 – 240V AC

## Slide 18: Electric Circuits for Control
Cooling Circuit
  12V DC computer fan
  Relay
  Powered by 12V DC

## Slide 19: Electric Circuits for Control
Probing Circuit
  1-wire thermistor
  Powered by 3.3V DC
Signaling Circuit
  Two relays
  Powered a 12V DC
Image credit: “Electronic Circuit” by Nicola Asuni is licensed under CC BY-SA 3.0

## Slide 20
Building a DIY Thermocycler
3.1 Parts and Tools

## Slide 21: Parts List (I)
Arduino UNO Rev3 Microcontroller Board
1-Wire Digital Temperature Sensor DS18B20
200W Incandescent Light Bulb and Socket
12V DC Computer Fan
Breadboard

## Slide 22: Parts List (II)
3-Prong Plug and Wires for Light Bulb Circuit
Variable Voltage AC/DC Adapter for Fan Circuit
Two 5V Relays with Daughter Board SRD-5VDC-SL-C
Jumper Wires
USB 2.0 A to USB 2.0 B Cable

## Slide 23: Tool Lists
Phillips Head Screwdriver (Cross-head)
Slot Head Screwdriver (Flat-blade)
Wire Cutter
3D-printer

## Slide 24
Building a DIY Thermocycler
3.2 Probing Circuit

## Slide 25: Testing of Each Part
Connect the 3.3V pin to the Uno board with the red pin of the 1-Wire thermistor using a jumper wire
Connect the GND pin to the Uno board with the black pin of the 1-Wire thermistor using a jumper wire

## Slide 26: Testing of Each Part
Connect the No.2 pin to the Uno board with the yellow pin of the 1-Wire thermistor using a jumper wire
Connect the No.2 pin on the Uno board with the yellow pin of the 1-Wire thermistor using a jumper wire

## Slide 27
Building a DIY Thermocycler
3.3 Heating Circuit

## Slide 28: Building Heating Circuit
Connect the coloured wires with the 3 pins insider the 3-prong plug
Image credit: “Plug Diagram” by Theresa Knott is licensed under CC BY-SA 2.5

## Slide 29: Building Heating Circuit
Connect the Live wire to the C port of the 1st relay
Connect another section of the Live wire to the NO port of the 1st relay
Connect the Earth wire to the Earth pin of the bulb socket
Attach the bulb to the bulb socket

## Slide 30
Building a DIY Thermocycler
3.4 Cooling Circuit

## Slide 31: Building Cooling Circuit
Connect a wire from the AC/DC adapter to the C port of the 2nd relay
Connect the NC port of the 2nd relay with one of the wires of the fan
Connect another wire of the fan with another wire of the AC/DC adapter

## Slide 32
Building a DIY Thermocycler
3.5 Signaling Circuit

## Slide 33: Signaling Circuit
Connect the 5V pin on the Uno board to the breadboard
Image credit: Photo by 1sfoerster is licensed under CC BY SA 3.0

## Slide 34: Signaling Circuit
Connect the two adjacent pins on the breadboard with the VCC pins on the two relays
Connect the GND pins on the two relays with another two GND pins on the Uno board
Image credit: “Electronic Circuit” by Nicola Asuni is licensed under CC BY-SA 3.0

## Slide 35: Signaling Circuit
Connect the IN pin on the first relay with the Pin No. 7 on the Uno board
Connect the IN pin on the second relay with the Pin No.4 on the Uno board
Image credit: “Electronic Circuit” by Nicola Asuni is licensed under CC BY-SA 3.0

## Slide 36
Building a DIY Thermocycler
3.6 Programme Code

## Slide 37: Uploading Code
Download the programme code (refer to the file “PCR_Arduino_Code_Cycle.txt”)
Connect the Uno Board to computer using a USB cable
Upload the programme code

## Slide 38
Building a DIY Thermocycler
3.7 Casing and Assembly

## Slide 39: Case Design
The case consist of 3 layers build with 4” PVC water pipe

## Slide 40: Bottom Layer
Drill a small hole for outgoing wire
Drill a rectangle hole for housing safety switch

## Slide 41: Middle Layer
Fit a 3D-printed coupling to the bottom part
Fit the middle PVC pipe casing to the coupling

## Slide 42: Middle Layer
Drill a hole in the middle of the PVC case
Use a nut and bolt to mount the light bulb socket and install a light bulb

## Slide 43: Middle Layer
Mount the fan on the outside of the middle layer casing
Connect all the wires

## Slide 44: Upper Layer
Fit a 3D-printed coupling to the middle casing
Fit the 3D-printed upper layer casing

## Slide 45
Thank you