## Slide 1
Jockey Club
STEAM Education Resources Sharing Scheme
WE Speak Louder
Unit 1
Studying a Loudspeaker

## Slide 2: Objectives
Describe the major components of a loudspeaker.
Measure the performance of a loudspeaker.
Discuss the characteristics of a loudspeaker.

## Slide 3: Introduction
Input Signals
Amplifier
Speaker
Block diagram of the key components of a loudspeaker

## Slide 4: Introduction

## Slide 5: How to Setup the Experiment?
Function Generator
Amplifier
Speaker
Oscilloscope

## Slide 6: How to Setup the Experiment?

## Slide 7: How to Setup the Experiment
Build your circuit as suggested in the video
Get a circuit as shown in below

## Slide 8: How to Measure Input and Output ?
Connect the input and output as suggested in the video
Use the oscilloscope to measure the input and output signals

## Slide 9: Change the Amplitude of Input and Observe the Variations of the Output

## Slide 10: Change the Frequency of Input and Observe the Variations of the Output

## Slide 11: Activity 1: Measuring the Input and Output Signals
Use the oscilloscope to find the amplitudes of input and output signals respectively.
Amplitude of Input signal voltage Vin | Vin = V
Amplitude of Output signal voltage Vout | Vout = V

## Slide 12: Activity 1: Measuring the Input and Output Signals
Use the oscilloscope to find the frequencies of input and output signals respectively.
Frequency of Input signal fin | fin = Hz
Frequency of Output signal fout | fout = Hz

## Slide 13: Activity 1: Measuring the Input and Output Signals
Find the gain of your amplifier. That is the ratio of the amplitudes of the output signal to the input signal = Vout / Vin

## Slide 14: Activity 1: Measuring the Input and Output Signals
Compare the shape of the waveforms of the input signal with the output signal. Are they the same? Yes or No?
Change the waveform of input in the function generator. What do you find about the shape of waveform in the oscilloscope?

## Slide 15: Activity 2: Changing Amplitude
Change the amplitude of input signal with function generator. Compare the input and output waveforms. What do you find? (e.g. the shape of waveform, amplitudes).
Listen to the sound coming from the speaker. What do you find? What about the loudness?

## Slide 16: Activity 3: Changing Frequency
Change the frequency of input signal in the function generator. Compare the input and output waveforms. What do you find?
Gradually increase the frequency of the input and listen to the sound coming from the speaker. What is the highest frequency of input that you can hear?
Compare your results with your classmate. Are they the same?

## Slide 17: Activity 3: Explaining the Results

## Slide 18: Activity 4: Modifying the Circuit

## Slide 19: Activity 4: Modifying the Circuit of Your Speaker
Modify the circuit as suggested in the video.

## Slide 20: Activity 4: Modifying the Circuit of Your Speaker
Repeat the measurement of output signals and record the results. What is the ratio of the amplitudes of output signal to input signal? i.e. Vout / Vin Vin = Vout = New gain of the speaker =

## Slide 21: Summary
Used function generator to produce an input signal and amplify the signal via the amplifier. The output signal was played through speaker.
Compared the input and output waveforms on the oscilloscope.
Investigated the effect of changing the amplitude and frequency of input signals.
learnt that there is limitation on the frequency that human ear can detect.
Modified the circuit to change the gain of the speaker.
You should have a better idea of characteristics of loudspeaker after this experiment

## Slide 22: Thank You