## Slide 1: Wind Powered Car
Jockey Club
STEAM Education Resources Sharing Scheme
Unit 1
Wind Powered Car

## Slide 2: Module Learning Outcomes
Upon the completion of the module, students should be able to:
Design a optimal propeller (螺旋槳) for the Wind Powered Car.
How to make the wind-powered car?
Wind Powered Car: Propeller
Materials Required

## Slide 3: Content
Class design
Implementation
Activity

## Slide 4: Class Design
Wind-powered car
Class design
Framework
Teaching plan
Implementation
Initiating motivation
Activity
Enquiry Learning
Research and study
Design
Construction
Testing
Investigation, analysis and discussion

## Slide 5: Framework
 | Mathematics | Science |  |  | Technology Education | Arts Education
Junior Form | Organization of data (MJ28.1-28.3) Presentation of data (MJ29.1-29.7) | Energy (SJ5.1-5.3) Making use of electricity (SJ8.1-8.4) |  |  | Materials and Resources (TK3.1-3.3) Tools and equipment (TK5.5-5.8) Production Process (TK6.1-6.5) Wind tunnel apps | Developing Creativity and Imagination employ a common procedure for visual arts making use sketching, drawing, information technology or other appropriate tools and resources to stimulate and develop ideas
 | Mathematics | Physics | Chemistry | Biology | ICT | 
Senior Form |  | Position and movement (SP2.1.1-2.1.6) Force and motion (SP2.2.1-2.2.4) Circuits and domestic electricity (SP4.2.4-4.2.6) |  |  |  | 

## Slide 6: Teaching plan
Motivation
Research and study
Reading articles about the concept of wind-powered car
Design
Drawing designs with sketches
Can any wind-powered car go directly downwind faster than the wind itself?
What does a wind-powered car look like?
What is its advantage vs conventional cars?
Researching current designs
Learning the theory, concept and relevant information
Understanding the car design using Wind Tunnel (Apps)
Discussion on the feasibility, pros and cons of the design
Finalizing the design
Construction
Constructing the propeller
Testing
Speed test
Investigation
Investigating effects of different propeller designs on the above tests
Analysis and Discussion
Discussing effects of different propeller designs on the above tests
Building the car chassis and shell
Assembling the car
Loading test
Uphill test
Investigating effects of different shape of car shells on the above tests
Discussing effects of different shape of car shells on the above tests
Suggestion on refining the car design
Conclusion based on own findings

## Slide 7: Enquiry Learning: a student-centered approach
Process | Element | 
Ask | Motivation | Can any wind-powered car go directly downwind faster than the wind itself? What does a wind-powered car look like? What is its advantage vs conventional cars?
Investigation | Research and study | Understanding the car design using Wind Tunnel
 | Investigation | Investigating effects of different propeller designs on the above tests Investigating effects of different shape of car shells on the above tests
Discuss | Design | Discussion on the feasibility, pros and cons of the design
 | Analysis and Discussion | Discussing effects of different propeller designs on the above tests Discussing effects of different shape of car shells on the above tests
Conclude | Analysis and Discussion | Conclusion based on own findings
Reflect | Design | Finalizing the design
 | Analysis and Discussion | Suggestion on refining the car design
Ask
Investigate
Discuss
Conclude
Reflect
Enquiry Learning

## Slide 8: Implementation
Wind-powered car
Class design
Framework
Teaching plan
Implementation
Initiating motivation
Activity
Enquiry Learning
Research and study
Design
Construction
Testing
Investigation, analysis and discussion

## Slide 9: Initiating motivation
There is an interesting science question that has been debated over a decade:
Can any wind-powered car can go faster than the wind itself that is pushing the car?
The answer was eventually unveiled in 2021…
15:26 - 16:50 Experimental result
17:30 - 20:20 Explanation
Source: Veritasium

## Slide 10: Initiating motivation
What does a wind-powered car look like?
What is its advantage vs conventional cars?

## Slide 11: Research and Study Reading
Are wind-powered cars a reality or just science fiction? (ampo.org)
Will These Wind-Powered Cars Be the Future of Travel? (news.lenovo.com)
https://ampo.org/are-wind-powered-cars-a-reality-or-just-science-fiction/
https://news.lenovo.com/chinook-wind-powered-cars-future-of-travel/

## Slide 12: Research and study Existing designs
Wind-powered
Sail-powered
Kite-powered
Rotor-powered

## Slide 13: Research and study Four forces
Thrust
Drag
Lift
Weight

## Slide 14: Research and study Four forces
Thrust is the driving force that move a vehicle in the direction of motion. In wind-powered car, the driving force is created by the motion of air.
Drag is the force that acts opposite to the direction of motion. It tends to slow an object. Drag is caused by frictions.

## Slide 15: Research and study Four forces
Weight is the force due to gravity. It acts toward the center of the Earth.
Lift is the force that holds a vehicle in the air. It is caused by the difference of pressure above and below the object.

## Slide 16: Research and study Four forces
When designing a vehicle, we want:
Weight > Lift : the vehicle will stay firmly on ground
Thrust > Drag: the vehicle will move forwards
Thrust
Drag
Lift
Weight

## Slide 17: Research and study Rotor-powered Vehicle
Take rotor-powered vehicle as an example to demonstrate how it work:
When moving from stationary, the vehicle is pushed by wind to create thrust. When thrust > drag (due to friction), it starts to move.
Thrust

## Slide 18: Research and study Rotor-powered Vehicle
When the vehicle is moving, if the speed of wind is still faster than the vehicle, the wind continues to push the vehicle forward → acceleration
Action force
Reaction force
Meanwhile the propeller are rotating, the wind will bounce back by the rotor blades creating an action-reaction pair. The kinetic energy of the wind (air molecules) transfer to the vehicle, making it moves faster.

## Slide 19: Research and study Rotor-powered Vehicle
Newton’s Laws of Motion:
1st law: An object at rest remains at rest, and an object in motion remains in motion at constant speed and in a straight line unless acted on by an unbalanced force.
2nd law: The acceleration of an object depends on the mass of the object and the amount of force applied.
3rd law: Whenever one object exerts a force on another object, the second object exerts an equal and opposite force on the first. (action-reaction force)

## Slide 20: Research and study Rotor-powered Vehicle
The wind pushes the vehicle forward, and once moving the wheels turn the propeller. The propeller spins in the opposite direction to that expected, pushing the wind backwards, which in turn pushes the car forwards, turning the wheels, and thus turning the propeller faster still.
Downwind Faster Than the Wind by Veritasium: How Does it Work (additional)?:
Wind-powered car goes down wind faster than the wind (phys.org)
Downwind Faster Than the Wind by Veritasium: How Does it Work? (youtube.com)

## Slide 21: Exercise 1 Experiencing Newton’s 3rd law
Aims: Understand how Newton’s 3rd law works
Materials: 1. Straw 2. Tape 3. String 4. Balloon
Procedures:
  Use a tape to attach a straw on the surface of a balloon.
  Pass a long string through the straw.
  Pump air into the balloon and then release.
  Observe the motion of the balloon and use your hand to feel the motion of the released air .

## Slide 22: Exercise 1 Experiencing Newton’s 3rd law
Result:
The balloon is moving to the _______(left/ right).
The air is pumped out to the _______(left/ right).
Analysis:
The balloon deflates and pushes the air towards (left/right).
The air exerts a reaction force on the balloon towards (left/right).
Hence, the balloon will move towards (left/right).
When the balloon ejects air in one direction, the air also pushes the balloon in the same (same/opposite) direction at the same time. <= This is the Newton’s 3rd law!

## Slide 23: Research and study Designing a car shell
The shape of a car shell has significant impact on the drag and lift force. The physics behind is out of our scope but we can still experience it using a simulation app called Wind Tunnel
Android: https://play.google.com/store/apps/details?id=com.algorizk.windtunnellite
iOS:
https://apps.apple.com/hk/app/wind-tunnel-free/id381971296?l=en-GB

## Slide 24: Research and study Designing a car shell
The direction of the wind
Flat head 平頭
Lift 升力=-0.48
Drag 阻力=21.87
Sharp head 尖頭
Lift 升力=0.76
Drag 阻力=9.65

## Slide 25: Research and study Designing a car shell
The direction of the wind
Bend downward 向下彎曲
Lift 升力=28.53
Drag 阻力=7.92
Bend upward 向上彎曲
Lift 升力=-43.46
Drag 阻力=11.82

## Slide 26: Research and study Designing a car shell
Remember what we want:
  Weight > Lift : the vehicle will stay firmly on ground
  Thrust > Drag: the vehicle will move forwards
Lower values of lift and drag are preferable !
Only lift can be negative value.
How should we design the car shell?

## Slide 27: Exercise 2 Designing the car shell
Aims:
Learn to use Wind Tunnel Free (iOS and Android app).
Understand how the shape will affect both drag and lift.
Procedures:
Open the app, select “Pressure” and “Wind Tunnel” mode.
Use “Draw” and “Erase” to design the car shell.
Press “Calculate” to measure the drag and lift, record these in the table provided.
Use “Reset” and draw another car shell.

## Slide 28: Exercise 2 Designing the car shell
Car design | Drag | Lift
Your own design: |  | 
Moving direction

## Slide 29: Research and study Designing the propeller

## Slide 30: Research and study Designing a propeller
There are numbers of factors that can be considered when designing a propeller:
The number of rotor blades;
The shape of the blades;
The material of the blades;
The tilt angle of the blades.

## Slide 31: Design
Drawing designs with sketches
Discussion on the feasibility, pros and cons of the design
Finalizing the design

## Slide 32: Activity
Wind-powered car
Class design
Framework
Teaching plan
Implementation
Initiating motivation
Activity
Enquiry Learning
Research and study
Design
Construction
Testing
Investigation, analysis and discussion

## Slide 33: Construction Materials
Cardboard
Motor
9V Battery and wiring
Craft sticks x 2
Paper Cup
Straws x 2
Wheels x 4

## Slide 34: Construction Build the chassis

## Slide 35: Construction Build the circuit

## Slide 36: Construction Build the circuit

## Slide 37: Construction Build the circuit

## Slide 38: Construction Build the circuit

## Slide 39: Construction Assembly

## Slide 40: Testing

## Slide 41: Testing

## Slide 42: Investigation and Analysis Speed test
0m
2m
Average speed is
where d is the travelling distance, i.e. d=2m
and t is the travelling time which is measured using stopwatch

## Slide 43: Investigation and Analysis Loading test
Place a 500g weight on the car. Then increase the number of weight one by one until the car cannot move. The loading can be treated as the number of weights N just before the car cannot move.
500g
500g
500g
500g
500g
500g
500g
N

## Slide 44: Investigation and Analysis Uphill test
For an uphill test, we can place the car on an uphill road with different tilt angle respectively. If the car can reach the top, it pass the test.
30o
45o
60o
50 cm

## Slide 45: Investigation
Investigating effects of different propeller designs
Investigating effects of different shape of car shells
Number of rotor blades | 2 blades | 3 blades | 4 blades | 5 blades
Speed test |  |  |  | 
Loading test |  |  |  | 
Uphill test |  |  |  | 
Car shell | Design 1 | Design 2 | Design 3 | Design 4
Speed test |  |  |  | 

## Slide 46: Analysis and Discussion
Discussing effects of different propeller designs on the above tests
Discussing effects of different shape of car shells on the above tests
Conclusions based on own findings
Suggestions on refining the car design

## Slide 47: Thank You