## Slide 1: UV, you and We
Jockey Club
STEAM Education Resources Sharing Scheme
Unit 4
UV in Laboratory

## Slide 2: Learning Objectives
Students should be able to:
use the DIY UV-box for disinfection and visualization purposes;
conduct the ATP-bacteria test;
conduct gel electrophoresis;
use thin layer chromatography.

## Slide 3: ATP-Bacteria Test
UV disinfection box
UV disinfection box
Product specification:
  Type of lamp: UVC LED
  Wavelength of UV used: 275 nm
  Time needed for disinfection: 15 – 30 mins
  Claimed to kill common bacteria up to 99.99 %
It is not so sophisticated as you thought!
Just try to make it by yourself!

## Slide 4: ATP-Bacteria Test
UV disinfection tools
UVC is used for disinfection by destroying some biological materials
such as DNA, RNA and proteins.
To make them unable to harm, reproduce or replicate.
Bacteria
Viruses
Surface protein
or antigen
Membrane
DNA or RNA
Source: Wikipedia – Bacteria by Ali Zifan licensed under CC BY-SA 4.0

## Slide 5: ATP-Bacteria Test
UV disinfection box
However, there are safety issues that need to pay attention!
1. Avoid direct exposure to UV especially UVB and UVC.
Our skin and eyes are sensitive to UV, which may cause adverse effects on us.
2. UVC can degrade some materials like plastic.
3. Strong UVC can generate ozone, which is an irritant to our respiratory tract.

## Slide 6: ATP-Bacteria Test
Adenosine triphosphate (ATP) is the universal energy molecule.
Bacterial cells
Yeast cells
Mold cells
Plants
Animals
ATP
In the environment, ATP should not be observed if there are no any living cells.
The presence of ATP
indicates
The presence of living cells
(including bacterial cells)

## Slide 7: ATP-Bacteria Test
Adenosine monophosphate
PPi
ATP
Detect the light intensity

## Slide 8: ATP-Bacteria Test
ATP test
Swabbing (5 x 5 cm2)
Less than 10 RLU = Clean
11 – 29 RLU = warning
Above 30 RLU = Dirty
UltraSnap Ensure

## Slide 9: ATP-Bacteria Test
UV disinfection box
Procedure
Sampling procedure:
Take one ATP sampling swab.
Swab the target object for sampling (Target area should be first determined and calculated for some large objects).
Swab the target object in two directions, the parallel one first and then the horizontal one.
Place the swab back in the swab tube.
Swabbing (e.g. 3 x 3 cm2)

## Slide 10: ATP-Bacteria Test
UV disinfection box
Measurement:
Before measurement, break the Snap-Valve, which is on top of the swab bending the bulb.
Shake the swab for 5 – 10 seconds.
Make sure that the liquid from the bulb contact with the swab bud while shaking.
After that, insert the entire swab tube into the luminometer within 30 seconds after shaking.
Record the result.
Luminometer
Procedure

## Slide 11: ATP-Bacteria Test
UV disinfection box
Test | 1 | 2 | 3
Target object |  |  | 
Swabbed area |  |  | 
Results (RLU) |  |  | 
Before UV disinfection using the DIY UV-box:
Procedure

## Slide 12: ATP-Bacteria Test
UV disinfection box
UV disinfection:
1. Place the interested object into the DIY UV-box.
2. Turn on the UV lamp for 10 minutes.
3. Turn off the UV lamp.
4. Take out the disinfected object.
5. Do the ATP-bacteria test again.
6. Compare the data obtained before and after the UV disinfection.
Procedure

## Slide 13: ATP-Bacteria Test
UV disinfection box
Test | 1 | 2 | 3
Target object |  |  | 
Swabbed area |  |  | 
Results (RLU) |  |  | 
(Results before disinfection) |  |  | 
After UV disinfection using the DIY UV-box:
Procedure

## Slide 14: Fluorescence
Fluorescence
What is fluorescence?
An object can emit light after it absorbed a particular wavelength of light or EM radiations.
Both emitted and absorbed light could be visible or invisible depending on the wavelength.
No light emission
With light emission (Fluorescence)
Source: Wikipedia -Fluorescent minerals licensed under CC BY-SA 2.5

## Slide 15: Fluorescence
Fluorescence
Examples of UV-active molecules
Aspirin – common drug
GelRed – commonly used in Biotechnology
Aspirin
Can absorb UV at ~230 nm wavelength
GelRed
Can absorb UV at ~300 nm wavelength
Then emit visible light at ~600 nm wavelength

## Slide 16: Gel Electrophoresis
What is Gel Electrophoresis?
It is a classical method to separate DNA molecules with different size.

## Slide 17: Gel Electrophoresis
DNA is loaded into the gel using auto-pipette
Since DNA is a charged molecule
Electric current attracts DNA moves from cathode and anode

## Slide 18: Gel Electrophoresis
There are pores inside the agarose gel
Large DNA will be trapped and move slower
Small DNA can pass through the pores easily and move faster
Separating DNA according to their sizes

## Slide 19: Gel Electrophoresis
Since DNA is not visible under normal light,
A chemical called GelRed is added to the DNA molecules
So that the DNA could be visualized under UV
And we can tell the size of the DNA molecules by comparing how far they move in a given time
Source: Yourgenome.org licensed under 4.0 CC-BY.
DNA molecules
with GelRed
Under UV radiation:

## Slide 20: Thin Layer Chromatography
What is Aspirin?
IUPAC name: 2-Acetoxybenzoic acid
Common name: Acetylsalicylic acid (ASA)
To inhibit fever, pain and inflammation
Aspirin

## Slide 21: Thin Layer Chromatography
How to make Aspirin?
Aspirin
+
Salicylic acid
Acetic anhydride
Acetic acid

## Slide 22: Thin Layer Chromatography
We need to heat up the mixture to drive the reaction.
However, how can we know when the reaction is finished?
Thin layer chromatography (TLC)
It is a aluminum film coated with some chemicals (e.g. silica gel, alumina).
The silica gel can attract molecules by polar-polar interaction.
Source: Thin Layer Chromatography by LibreTexts license under CC BY-NC-SA 4.0

## Slide 23: Thin Layer Chromatography
The solvent will also “push” the molecules to move.
The molecule that is attracted strongly by the silica gel will move slower.
Another molecule that is just slightly attracted by the silica gel will move faster.
Therefore, we can separate different molecules by using TLC.
However, most of the molecules are not visible under normal light.
Therefore, we need to use UV to visualize the molecules (Fluorescence).
Thin layer chromatography (TLC)
Source: Thin Layer Chromatography by LibreTexts license under CC BY-NC-SA 4.0

## Slide 24: Thin Layer Chromatography
Thin layer chromatography (TLC)
TLC under UV (Fluorescence)
Animation
Source: Thin Layer Chromatography by LibreTexts license under CC BY-NC-SA 4.0

## Slide 25: Thin Layer Chromatography
How to make Aspirin?
Aspirin
+
Salicylic acid
Acetic anhydride
Acetic acid
This group is an UV-active group.

## Slide 26: Thin Layer Chromatography
TLC under UV (Fluorescence)
We will use our UV-box to visualize the TLC.
Source: Thin Layer Chromatography by LibreTexts license under CC BY-NC-SA 4.0
Thin layer chromatography (TLC)

## Slide 27: Thin Layer Chromatography
S
M
P
Add a drop of salicylic acid
on position “S” and “M”.
Add a drop of reaction mixture
on position “M” and “P”.
???
Thin layer chromatography (TLC)

## Slide 28: Thin Layer Chromatography
S
M
P
Add a drop of salicylic acid
on position “S” and “M”.
Add a drop of reaction mixture
on position “M” and “P”.
???
Before the start of reaction
After 5 min of the reaction started
After 15 min of the reaction started
Do it three times
Thin layer chromatography (TLC)

## Slide 29: Thin Layer Chromatography
S
M
P
S
M
P
S
M
P
At the beginning
After 15 min
After 30 min
Time
What do these three TLC mean?
Thin layer chromatography (TLC)

## Slide 30: Thin Layer Chromatography
S
M
P
S
M
P
S
M
P
Case 1
Case 2
Case 3
Thin layer chromatography (TLC)

## Slide 31: Summary
The DIY UV-box is used for the following activities:
  ATP-bacteria test;
  Gel electrophoresis;
  Thin layer chromatography.

## Slide 32
Thank you