## Slide 1: Dancer in water – Microalgae
Jockey Club
STEAM Education Resources Sharing Scheme
Unit 2 – cultivation of microalgae

## Slide 2: Objectives
Isolate microalgae in environmental water samples
Select and use appropriate skills in cultivating single strain of microalgae
Conduct microalgal counting with a microscope

## Slide 3: Microalgae in the natural environments
Microalgae exist in various types of natural environments
To study them, we could
  Conduct field survey
  Maintain lab cultures & carry out experiments  cultivation of microalgae

## Slide 4: Tools/materials for the cultivation of microalgae
Autopipette
Culture flask
Culture medium
Agar plate
Bunsen burner
Microscope

## Slide 5: Basic techniques of pipetting
Suggested steps of proper pipetting:
Set the volume on the pipette.
Press the plunger to the first stop and hold the position.
Immerse the tip to the correct depth, which can vary by the pipette and tip, and smoothly release the plunger.
Wait about 1 second for the liquid to flow into the tip.
Position the pipette tip inside the receiving container and smoothly press the plunger to the second stop to release the solution.
Allow the plunger to return to its rest position.
Properly discard the used pipette tip.
Source: Andy Connelly licensed under CC BY-SA 4.0 DEED

## Slide 6: Basic techniques of pipetting
Source: Andy Connelly licensed under CC BY-SA 4.0 DEED

## Slide 7: Isolation of microalgal cells
To isolate microalgal cells from environmental samples
Streak/spread plate method
Serial dilution method
Single cell isolation
Mono-species clonal microalgae culture

## Slide 8: Aseptic techniques
To create a sterilized workspace with a Bunsen burner
Carry out all the works within the sterile area

## Slide 9: Streak/Spread Plate Method (條紋 / 擴散板法)
https://www.youtube.com/watch?v=EkDVq4rl30U

## Slide 11: Suggested steps of streak plate method
Disinfect work surface with 70% ethanol.
After the disinfectant has dried completely, turn on the Bunsen burner and handle samples within the clean area of the flame.
Sterilize the inoculating loop by putting the loop into the flame of the Bunsen burner. Wait for the loop to turn red and let it cool down for a few moments.
Transfer a volume (e.g., 100 µL) of diluted environmental samples to an agar plate with autopipette.
Gently streak the inoculating loop with a back-and-forth motion in the first quarter of the agar plate.
Put the loop in the flame and let it cool. Extend the streaks into the second quarter of the petri plate.
Repeat step 6 for the third and fourth quarters of the agar plate.
Sterilize the loop again after streaking all quarters.
Seal the petri dish with parafilm. Position the petri dish upside-down.
Incubate the agar plates at the appropriate temperature and light condition.
Disinfect work surface again with 70% ethanol.

## Slide 13: Suggested steps of spread plate method
Disinfect work surface with 70% ethanol.
After the disinfectant has dried completely, turn on the Bunsen burner and handle samples within the clean area of the flame.
Dip the L-shaped glass spreader into 70% ethanol.
Flame the L-shaped glass spreader over a Bunsen burner and let it cool down for a few moments.
Transfer a volume (e.g., 100 µL) of diluted environmental samples to an agar plate.
Spread the sample evenly over the surface of agar using the sterile glass spreader, carefully rotating the petri dish underneath at the same time.
Seal the petri dish with parafilm. Position the petri dish upside-down.
Incubate the agar plates at the appropriate temperature and light condition.
Disinfect work surface again with 70% ethanol.

## Slide 14: Serial Dilution Method (連續稀釋法)
1mL
1mL
1mL
1mL
1mL
Environmental sample
Each tube: 9mL medium + 1mL aliquot of each dilution
10-1
10-2
10-3
10-5
10-4
Dilutions

## Slide 15: Single Cell Isolation (單細胞分離法)
50ml algae culture by using plankton net
Single cell isolation by 10 µl micropipette
96 well plate
Flask culturing
48 well plate/24 well plate

## Slide 16: Cultivation of microalgae
After the microalgae cells are isolated and the initial microalgae cultures are established.
Maintenance and propagation of microalgae cultures
Source: Bulk Microalgae | UTEX Culture Collection of Algae licensed under CC BY-NC-ND 4.0 DEED

## Slide 17: Factors on the growth of microalgae
Light
Temperature
Nutrients (N & P)
Salinity
pH
Water mixing
Source: Wikipedia – bioreactor licensed under CC BY-SA 4.0

## Slide 18: Tools and materials
Container
Microalgae
Medium 培養液 = Water + Nutrients + trace metal elements + vitamins
Pipettes
How to sterilize?

## Slide 19: Culture medium (培養液)
No | Stock solution |  | Dissolved to 15mL DI water (g) | Dissolved to 50mL DI water (g) | Add ? ml for 500mL medium
1 | MgNa2EDTA |  |  | 0.05 | 0.5 ml
2 | Trace metal solution A | H3BO3 |  | 0.143 | 0.5 ml
 |  | MnCl2 ∙4H2O |  | 0.0905 | 
 |  | ZnSO4 ∙7H2O |  | 0.011 | 
 |  | NaMoO4 ∙2H2O |  | 0.01955 | 
3 | Trace metal solution B | CuSO4 ∙5H2O | 0.1185 |  | 0.5ml (1:100)
 |  | Co(NO3)2 ∙6H2O | 0.0741 |  | 
4 | Fe citrate solution | i. Citric acid |  | 0.3 | 0.5 ml
 |  | ii. Ferric ammonium citrate |  | 0.3 | 
5 | NaNO3 |  |  | 15 | 2.5 ml
6 | K2HPO4 ∙3H2O |  |  | 2 | 0.5 ml
7 | MgSO4 ∙7H2O |  |  | 3.75 | 0.5 ml
8 | CaCl2 ∙2H2O |  |  | 1.8 | 0.5 ml
9 | Na2CO3 |  |  | 1 | 0.5 ml

## Slide 20: Culture medium (培養液)
No | Stock solution |  | Dissolved to 15mL DI water (g) | Dissolved to 50mL DI water (g) | Add ? ml for 500mL medium
1 | MgNa2EDTA |  |  | 0.05 | 0.5 ml
2 | Trace metal solution A | H3BO3 |  | 0.143 | 0.5 ml
 |  | MnCl2 ∙4H2O |  | 0.0905 | 
 |  | ZnSO4 ∙7H2O |  | 0.011 | 
 |  | NaMoO4 ∙2H2O |  | 0.01955 | 
3 | Trace metal solution B | CuSO4 ∙5H2O | 0.1185 |  | 0.5ml (1:100)
 |  | Co(NO3)2 ∙6H2O | 0.0741 |  | 
4 | Fe citrate solution | i. Citric acid |  | 0.3 | 0.5 ml
 |  | ii. Ferric ammonium citrate |  | 0.3 | 
5 | NaNO3 |  |  | 15 | 2.5 ml
6 | K2HPO4 ∙3H2O |  |  | 2 | 0.5 ml
7 | MgSO4 ∙7H2O |  |  | 3.75 | 0.5 ml
8 | CaCl2 ∙2H2O |  |  | 1.8 | 0.5 ml
9 | Na2CO3 |  |  | 1 | 0.5 ml
20

## Slide 21: Sterilization of tools/materials
Autoclave 高壓滅菌 (121oC, 20 mins)
Microwave sterilization 微波殺菌 (Total time=5mins) (2,1,2 mins of treatment with 30s intervals)
Ultraviolet radiation 紫外線滅菌
Filtration 過濾殺菌 (Syringe filter/top-up filter, 0.22um)
21

## Slide 22: Preparing your own culture medium
Add nutrients to sterilized water to make a culture medium
With aseptic techniques
Nutrient stocks
Tissue culture flask

## Slide 23: Suggested steps of medium preparation
Disinfect work surface with 70% ethanol.
After the disinfectant has dried completely, turn on the Bunsen burner and handle solutions within the clean area of the flame.
Flame the neck and cap bottles by passing them through a hot Bunsen burner flame several times.
Transfer the correct volumes of stock solutions separately using autopipette to the autoclaved water.
Flame the neck and cap of bottles again.
Mix the solution by inverting the closed bottle up and down several times.
Disinfect work surface again with 70% ethanol.

## Slide 24: Growth phases of microalgae
Induction phase (遲緩期):
  Physiological adaptation of the cell metabolism for growth
Exponential phase (對數期):
  Cell no. rapidly increases
Phase of declining relative growth
  Due to the nutrient limitation
Stationary phase (穩定期)
  Cell division rate = death rate
Death phase (衰亡期)
  Due to nutrient depletion, oxygen deficiency, pH change and toxic metabolite accumulation
Source: http://www.fao.org/3/w3732e/w3732e06.htm#2.3.%20Algal%20production

## Slide 25: Sub-culturing microalgae
To maintain healthy populations of microalgae in cultures and enable the continuous propagation of the microalgae by transferring a stock culture to a fresh culture medium
Source: http://www.fao.org/3/w3732e/w3732e06.htm#2.3.%20Algal%20production
Fresh culture medium
Old microalgae stock culture

## Slide 26: Suggested steps of sub-culturing
Prepare fresh culture medium with the proper steps.
Adjust the medium to the culturing temperature.
Disinfect work surface with 70% ethanol.
After the disinfectant has dried completely, turn on the Bunsen burner and handle solutions within the clean area of the flame.
Flame the neck and cap bottles by passing them through a hot Bunsen burner flame several times.
Transfer the 10% volume of the original microalgae culture to the fresh medium.
Flame the neck and cap of bottles again.
Incubate the culture at the appropriate temperature and light condition.
Disinfect work surface again with 70% ethanol.

## Slide 27: Counting microalgae samples
https://www.youtube.com/watch?v=PMvzK5G-G7M

## Slide 28: Sedgewick Rafter Counting Chamber
A total of 1000 grids in the counting chamber.
Count only a portion of them

## Slide 29: Counting Individual Cell
For colony-forming microalgae
Each arrow indicates 1 single cell.

## Slide 30: Suggested steps of counting cells using the Sedgewick-Rafter counting chamber
Mix the preserved sample by slowly inverting the closed sample container several times.
Use an autopipette to draw 1 mL of the sample and slowly load it on the Sedgewick-Rafter counting chamber.
Position the cover slide in place. Make sure no air bubbles are trapped underneath the slide.
Wait for approximately 3 minutes to allow the microalgal cells to settle onto the bottom layer of the counting chamber.
Count the number of microalgal cells in a certain number of small grids of the counting chamber. In case that microalgal cells are settled on the edges of the small grids, count only the cells overlapping the right-hand and top boundaries.

## Slide 31: Suggested steps of counting cells using the Sedgewick-Rafter counting chamber
6. Calculate the cell density of microalgae (D, cells/mL) in cultures as
where n = the number of cells counted and p = the proportion of the number of counted small grids to 1000 grids.
Calculate the cell densities of microalgae cultures collected at different time points.
Estimate the growth rate (r, /day) of microalgae cultures as
where Dt = cell density at time t, D0 = cell density at previous time point, and t = time intervals in days.

## Slide 32: Growth phases of microalgae
Induction phase (遲緩期):
  Physiological adaptation of the cell metabolism for growth
Exponential phase (對數期):
  Cell no. rapidly increases
Phase of declining relative growth
  Due to the nutrient limitation
Stationary phase (穩定期)
  Cell division rate = death rate
Death phase (衰亡期)
  Due to nutrient depletion, oxygen deficiency, pH change and toxic metabolite accumulation
Source: http://www.fao.org/3/w3732e/w3732e06.htm#2.3.%20Algal%20production

## Slide 33: Estimating the growth of microalgae
For sample at Dt
1 mL sample + 0.2 mL Lugol’s solution
Number of grids counted: 50
Number of algal cells counted: 600
For sample at D0
1 mL sample + 0.2 mL Lugol’s solution
Number of grids counted: 50
Number of algal cells counted: 150
 Dt = 14,400 cells/mL
 D0 = 3,600 cells/mL

## Slide 34: Estimating the growth of microalgae
To calculate the growth rate (r)
r = 0.46/day
34
D0
Dt
t = 3 days
Exponential phase

## Slide 35: Factors on the growth of microalgae
Light
Temperature
Nutrients (N & P)
Salinity
pH
Water mixing
 | Treatment 1 | Treatment 2 | Treatment 3
Light (µE m-2 s-1) | 100 | 100 | 100
Temperature (°C) | 20 | 23 | 26
Salinity (psu) | 30 | 30 | 30
Growth rate (/day) | 0.46 | ??? | ???

## Slide 36: Summary
Isolation of microalgal cells
Cultivation of microalgae cultures
Counting microalgal cells and estimating the growth rate of them