## Slide 1
STEAM Activity and Experiment: Science Investigation x Micro:bit

## Slide 2: Introduction
3. What is the most difficult part of designing a STEAM activity?
1. How many of you did this before?
2. What kinds of STEAM activity you want your
students to participate in?

## Slide 3: Introduction
Science investigation:
Variables
Time
Temp.
Angle
pH
Light
Rate
Speed
Turbidity

## Slide 4: Introduction
Science investigation:
Variables
Time
Temp.
Angle
pH
Light
Rate
Speed
Turbidity
Tools
Measure

## Slide 5: Introduction
Science investigation:
Variables
Tools
Measure
STEAM

## Slide 6: Introduction
https://nixbiosensors.com/

## Slide 7: Introduction

## Slide 8: Introduction
https://www.grow-green.com/product/aspara-nature-smart-grower-hk/

## Slide 9: Introduction
+
IoT

## Slide 10: Introduction
After this workshop, you will be able to:
Write easy programs by using “makecode”
Assemble the sensors, electronic parts and micro:bit for science investigation
3. Sensor calibration
4. Add the TEAM elements to Science

## Slide 11: Introduction
Programming: By using makecode/micro:bit
We are going to make:
  Timer
  Light sensor and light bulb
  Temperature and water temperature sensor
  Turbidity sensor
  Flow rate meter
All sensors and parts are safe, cheap, easy-to-use and compatible to micro:bit
Source: Wikipedia licensed under CC0

## Slide 12: Introduction
Source: Micobit.org

## Slide 13: Coding
1. Bluetooth connection
Download the app “micro:bit”

## Slide 14: Coding
Click “Manage Connections”
Then “Pair a micro:bit”

## Slide 15: Coding
Reset
Press and release the “reset” button 3 times

## Slide 16: Coding
COPY the LED columns from you micro:bit
Enter the same pattern to the app

## Slide 17: Coding
1 and 0
1
0

## Slide 18: Coding
Start
Stop
Display
Something that can
change with time
Reset
Makecode website: makecode.microbit.org
1. Timer

## Slide 19: Coding
Something that can
change with time
Display
Start
Stop
Reset
Makecode website: makecode.microbit.org
1. Timer

## Slide 20: Coding
Download the program
to micro:bit

## Slide 21: Coding
LED display at the same time a light sensor
Makecode website: makecode.microbit.org
2. Light sensor

## Slide 22: Coding
Download the program
to micro:bit
Automation: Do something by itself after receiving some information or data
Makecode website: makecode.microbit.org
2. Light sensor

## Slide 23: Coding
I/O Pin
Input/output pin
In micro:bit:
“Read” = Input to micro:bit
“Write” = Output from micro:bit
Makecode website: makecode.microbit.org
2. Light sensor and LED light bulb

## Slide 24: Coding
Download the program
to micro:bit
I/O Pin
Makecode website: makecode.microbit.org
2. Light sensor and LED light bulb

## Slide 25: Coding
I/O Pin
1
0
Makecode website: makecode.microbit.org

## Slide 26: Assemble of Sensors and Parts
- to G
+ to S
Use Pin 0
2. Light sensor and LED light bulb

## Slide 27: Coding
Makecode website: makecode.microbit.org
3. Temperature sensor
Temperature sensor inside the CPU

## Slide 28: Coding
Download the program
to micro:bit
Makecode website: makecode.microbit.org
3. Temperature sensor

## Slide 29: Coding
You cannot immerse your micro:bit into water
3. Water temperature sensor
Makecode website: makecode.microbit.org
Temperature sensor inside the CPU

## Slide 30: Coding
For light and temp., they are built-in sensors
Now, we are using external sensor
E.g.
  Water temperature
  Ethanol
  Carbon dioxide
  IR
3. Water temperature sensor
Makecode website: makecode.microbit.org
  UV
  Motion
  pH

## Slide 31: Coding
Very useful searching engine
You can search any pre-set coding or program available or not
Any coding for different sensors
3. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 32: Coding
Search: https://github.com/DFRobot/pxt-ds18b20
3. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 33: Coding
3. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 34: Coding
DAT
VCC
GND
3. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 35: Coding
Pin no.
G
V
S
3. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 36: Coding
For light and temp., they are built-in sensors
Now, we are using external sensor
E.g.
  Water temperature
  Ethanol
  Carbon dioxide
  IR
4. Water turbidity sensor
Makecode website: makecode.microbit.org
  UV
  Motion
  pH

## Slide 37: Coding
What will be changed if the water turbidity changed?
4. Water turbidity sensor
Makecode website: makecode.microbit.org
Turbidity Standard: https://www.dosiclor.com/turbidity-standard-product-line/

## Slide 38: Coding
Light emitter
To detect the light scattering
4. Water turbidity sensor
Makecode website: makecode.microbit.org

## Slide 39: Coding
Makecode website: makecode.microbit.org
I/O Pin
Input/output pin
In micro:bit:
“Read” = Input to micro:bit
“Write” = Output from micro:bit
4. Water turbidity device

## Slide 40: Coding
Makecode website: makecode.microbit.org
I/O Pin
Input/output pin
In micro:bit:
“Read” = Input to micro:bit
“Write” = Output from micro:bit
4. Water turbidity device

## Slide 41: Coding
Makecode website: makecode.microbit.org
4. Water turbidity device
Download the program
to micro:bit

## Slide 42: Assemble of Sensors and Parts
Jump wires
micro:bit breakout board
micro:bit
2x 3A battery box
with switch
Turbidity sensor
micro:bit
Breakout board
Jump wires
Turbidity sensor
2x 3A battery box
with switch
Material list
4. Water turbidity device

## Slide 43: Assemble of Sensors and Parts
Only use 1,2 and 3
but not 4
G to G
V to V
A to S
Use Pin 2
4. Water turbidity device

## Slide 44: Testing and Calibration
Calibration:
The sensor only gives you a range of number (e.g. from 0 – 1000)
The number actually is depending on the turbidity of liquid
We need to change the number to turbidity
Clarity
Sensor
250
1
Turbidity level
10
1
4. Water turbidity device

## Slide 45: Testing and Calibration
Preparation：
  Water
  Milk
Measurement:
  Place the sensor into the liquid
  Record down the number displayed
Water：______________
Milk：______________

## Slide 46: Testing and Calibration
Calibration:
4. Water turbidity device
Modify the code by using:
and

## Slide 47: Testing and Calibration
Calibration:
4. Water turbidity device
Milk：_____ Water：_____
Enter the values you have obtained before!

## Slide 48: Coding
5. Flow rate meter

## Slide 49: Coding
5. Flow rate meter
P0
P1
P2
The P0 position is set to “always on”
(always supply electricity)
The P1 and P2 positions are set to “off”
(No electricity supply)

## Slide 50: Coding
5. Flow rate meter
Water out
Ready
With table
salt added
Although P1 and P2 are set to “off”,
electricity from P0 could be transmitted to P1 and P2 and turn them “on” via water with table salt added

## Slide 51: Coding
Water out
Meter Start
Meter Stop
Ready
Water out
Water out
5. Flow rate meter

## Slide 52: Coding
P0
P1
P2
5. Flow rate meter

## Slide 53: Assemble of Sensors and Parts
11 cm
8 cm
5 cm
Copper rod
3 cm
3 cm
3 cm
3 cm
3 cm
2 cm

## Slide 54: Assemble of Sensors and Parts
3 cm
3 cm
3 cm
3 cm
1.5 cm
4 cm
2x
3 cm
3 cm

## Slide 55: Testing
Test your flow rate meter by using a cup of water
  Moving up the meter
Meter Start
Meter Stop
Ready

## Slide 56: Flow Rate
Water out
Water out
Start
Stop
Flow Rate Measurement
Flow rate = Water out (ml) / time required
Time required: Counted by the flow rate meter
Water out (ml): ???
3 cm
The diameter of the bottle: 7 cm
The length difference: 3 cm
Volume of cylinder:
Water out: 3
Water out: ~115 cm3
Flow rate = 115 ml / time required
7 cm

## Slide 57: Conclusion
Now you can:
Write easy programs by using “makecode”
Assemble the sensors, electronic parts and micro:bit for science investigation
3. Sensor calibration
4. Add the TEAM elements to Science

## Slide 58
Jockey Club STEAM Education Resources Sharing Scheme 賽馬會STEAM教育資源共享計劃

## Slide 59: Jockey Club STEAM Education Resources Sharing Scheme
4 years project
Funded by The Hong Kong Jockey Club Charities Trust
Work together with secondary schools
Providing relevant support to secondary schools to implement STEAM education
Development of STEAM related materials
Student learning activities
Teachers’ professional development
An information hub for sharing good practices

## Slide 60: Useful Links
Enquiry:
Phone: 2768 6804
Email: steam@hkmu.edu.hk
Our website
List of Modules
List of Workshops