## Slide 1
STEAM Activity : Biology x Micro:bit

## Slide 2: Introduction
3. What is the most difficult part of designing a STEAM activity?
1. How many of you did this before?
2. What kinds of STEAM activity you want your
students to participate in?

## Slide 3: Introduction
Investigation of biological experiment:
Variables
Time
Temp.
CO2
pH
Light
Rate
Speed
Turbidity

## Slide 4: Introduction
Investigation of biological experiment:
Variables
Time
Temp.
CO2
pH
Light
Rate
Speed
Turbidity
Tools
Measure

## Slide 5: Introduction
Investigation of biological experiment:
Variables
Tools
Measure
STEAM

## Slide 6: Introduction
Practical 5.2: Investigation of the effect of temperature on enzyme activity
Objective: To study the effect of temp. on amylase activity
20 oC
40 oC
60 oC
80 oC
100 oC

## Slide 7: Introduction
pH = 3
pH = 4
pH = 5
pH = 6
pH = 7
Practical 5.3: Investigation of the effect of pH on enzyme activity
Objective: To study the effect of pH on amylase activity
Acidic
Alkaline
pH Scale

## Slide 8: Introduction
Inhaled air
Exhaled air
Hydrogencarbonate indicator
Practical 8.5: Comparison of the carbon dioxide content of inhaled air and exhaled air
Objective: To compare the CO2 content

## Slide 9: Introduction
Quantify the light intensity by using
LED display at the same time a light sensor
Distance
Practical 21.7: Investigation of the effect of light intensity on the rate of photosynthesis
Objective: To study the effect of light intensity

## Slide 10: Introduction
https://ketoair.com/

## Slide 11: Introduction
https://nixbiosensors.com/

## Slide 12: Introduction

## Slide 13: Introduction
https://www.grow-green.com/product/aspara-nature-smart-grower-hk/

## Slide 14: Introduction
+
IoT

## Slide 15: Introduction
After this workshop, you will be able to:
Write easy programs by using “makecode”
Assemble the sensors, electronic parts and micro:bit for science investigation
3. Sensor calibration
4. Add the TEAM elements to S (Biology)

## Slide 16: Introduction
Programming: By using makecode/micro:bit
We are going to make:
  Light sensor and light bulb
  Temperature and water temp. sensor
  Turbidity sensor
  Colonometer
All sensors and parts are safe, cheap, easy-to-use and compatible to micro:bit
An infection game using micro:bit (if possible)
Source: Wikipedia licensed under CC0

## Slide 17: Introduction
Source: Micobit.org

## Slide 18: Coding
1. Bluetooth connection
Download the app “micro:bit”

## Slide 19: Coding
Click “Manage Connections”
Then “Pair a micro:bit”

## Slide 20: Coding
Reset
Press and release the “reset” button 3 times

## Slide 21: Coding
COPY the LED columns from you micro:bit
Enter the same pattern to the app

## Slide 22: Coding
1 and 0
1
0

## Slide 23: Coding
LED display at the same time a light sensor
Makecode website: makecode.microbit.org
1. Light sensor

## Slide 24: Coding
Download the program
to micro:bit
Automation: Do something by itself after receiving some information or data
Makecode website: makecode.microbit.org
1. Light sensor

## Slide 25: Coding
I/O Pin
Input/output pin
In micro:bit:
“Read” = Input to micro:bit
“Write” = Output from micro:bit
Makecode website: makecode.microbit.org
1. Light sensor

## Slide 26: Coding
Makecode website: makecode.microbit.org
1. Light sensor and LED light bulb
Download the program
to micro:bit
I/O Pin

## Slide 27: Coding
I/O Pin
1
0
Makecode website: makecode.microbit.org

## Slide 28: Assemble of Sensors and Parts
- to G
+ to S
Use Pin 0
1. Light sensor and LED light bulb

## Slide 29: Coding
Makecode website: makecode.microbit.org
2. Temperature sensor
Temperature sensor inside the CPU

## Slide 30: Coding
Download the program
to micro:bit
Makecode website: makecode.microbit.org
2. Temperature sensor

## Slide 31: Coding
You cannot immerse your micro:bit into water
2. Water temperature sensor
Makecode website: makecode.microbit.org
Temperature sensor inside the CPU

## Slide 32: Coding
For light and temp., they are built-in sensors
Now, we are using external sensor
E.g.
  Water temperature
  Ethanol
  Carbon dioxide
  IR
2. Water temperature sensor
Makecode website: makecode.microbit.org
  UV
  Motion
  pH

## Slide 33: Coding
Very useful searching engine
You can search any pre-set coding or program available or not
Any coding for different sensors
2. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 34: Coding
Search: https://github.com/DFRobot/pxt-ds18b20
2. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 35: Coding
2. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 36: Coding
DAT
VCC
GND
2. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 37: Coding
Pin no.
G
V
S
2. Water temperature sensor
Makecode website: makecode.microbit.org

## Slide 38: Coding
For light and temp., they are built-in sensors
Now, we are using external sensor
E.g.
  Water temperature
  Ethanol
  Carbon dioxide
  IR
3. Water turbidity sensor
Makecode website: makecode.microbit.org
  UV
  Motion
  pH

## Slide 39: Coding
What will be changed if the water turbidity changed?
3. Water turbidity sensor
Makecode website: makecode.microbit.org
Turbidity Standard: https://www.dosiclor.com/turbidity-standard-product-line/

## Slide 40: Coding
Light emitter
To detect the light scattering
3. Water turbidity sensor
Makecode website: makecode.microbit.org

## Slide 41: Coding
Makecode website: makecode.microbit.org
I/O Pin
Input/output pin
In micro:bit:
“Read” = Input to micro:bit
“Write” = Output from micro:bit
3. Water turbidity device

## Slide 42: Coding
Makecode website: makecode.microbit.org
I/O Pin
Input/output pin
In micro:bit:
“Read” = Input to micro:bit
“Write” = Output from micro:bit
3. Water turbidity device

## Slide 43: Coding
Makecode website: makecode.microbit.org
3. Water turbidity device
Download the program
to micro:bit

## Slide 44: Assemble of Sensors and Parts
Jump wires
micro:bit breakout board
micro:bit
2x 3A battery box
with switch
Turbidity sensor
micro:bit
Breakout board
Jump wires
Turbidity sensor
2x 3A battery box
with switch
Material list
3. Water turbidity device

## Slide 45: Assemble of Sensors and Parts
Only use 1,2 and 3
but not 4
G to G
V to V
A to S
Use Pin 2
3. Water turbidity device

## Slide 46: Testing and Calibration
Calibration:
The sensor only gives you a range of number (e.g. from 0 – 1000)
The number actually is depending on the turbidity of liquid
We need to change the number to turbidity
Clarity
Sensor
250
1
Turbidity level
10
1
3. Water turbidity device

## Slide 47: Testing and Calibration
Preparation：
  Water
  Milk
Measurement:
  Place the sensor into the liquid
  Record down the number displayed
Water：______________
Milk：______________

## Slide 48: Testing and Calibration
Calibration:
3. Water turbidity device
Modify the code by using:
and

## Slide 49: Testing and Calibration
Calibration:
3. Water turbidity device
Milk：_____ Water：_____
Enter the values you have obtained before!

## Slide 50: Coding
4. Colonometer
Colony Counter
It is used to count the colonies formed on a petri dish
After performing the spread plate experiment
Colony counter/colonometer
Check product image here
https://www.carlroth.com/com/en/colony-counters-hand-held-colony-counters/colony-counter-sc6-plus/p/en38.1
1. Number display
2. Place for the dish
with a sensor
3. Magnifying glass
~ $8000 HKD

## Slide 51: Coding
Colony Counter
It is used to count the colonies formed on the petri dish
After performing the spread plate experiment
Spread plate
experiment:
Place the dish on the counter
Use a pen for counting
By pressing the dish
The counter possess a sensor
that can sense pressure/touching/force

## Slide 52: Coding
To make it, what you need:
A processor
A display
A sensor
A program
Micro:bit
It is a processor
with a simple display

## Slide 53: Coding
To make it, what you need:
A processor
A display
A sensor
A program
DIY pressure sensor
Mechanism:
The two paper cardboards are connected with wires
by conductive tapes
The two cardboards are barely separated by using
springs and Blu-tack between the two boards
Once you press it, the conductive tapes will be forced to connect
and close the circuit
Press it!
Press it to
close the circuit

## Slide 54: Coding
Press it!
Press it to
close the circuit
and
send the signal
DIY pressure sensor
6.5 – 7 cm

## Slide 55: Coding
= What is the basic setting at the beginning
= To supply electricity to pin (P0, 1 or 2)
“1” = Yes while “0” = No
= To ask the display to show number
of the counter (a variable we set)

## Slide 56: Coding
= How the program runs
= We will connect our sensor to P1
= To see whether the circuit of the sensor is
closed or not (being pressed or not)
If yes, P1 will have electricity (become “1”)
If not, P1 will not have electricity (remain “0”)
= Set the program to check the electricity of P1
If P1 is “1”, the program will change the counter by 1
If not, the program will change the counter by 0
= To ask the display to show number
of the counter (a variable we set)

## Slide 57: Coding
= There is a button called A on each micro:bit
Button A
Button B
= Set the program to reset the counter display
to 0 when we press the button A
Press
button A

## Slide 58: Coding

## Slide 59: Coding
The most difficult part:
A processor
A display
A sensor
A program
Two common situations:
The sensor is not sensitive enough
i.e. Press is not
counted/hard press
is needed
The sensor is too
sensitive
i.e. Counted 1 when
there is no press

## Slide 60: Coding
The sensor is not sensitive enough
i.e. Press is not
counted/hard press
is needed
The sensor is too
sensitive
i.e. Counted 1 when
there is no press
Try to minimize the distance between two paper cardboards by using less blu-tack
Try to increase the distance between two paper cardboards by using more blu-tack or longer springs
Adjust your sensor
by trial and error!

## Slide 61: Infection Game
Game Rules:
All of you are citizens
One of you will be randomly assigned as “Patient Zero”
Try to find out who is the “Patient Zero” at the end
Citizen

## Slide 62: Infection Game
Game Rules:
Each of you will need to play “Rock-paper-scissors” with 5 citizens
Please put your micro:bit together while playing
You can only leave the other player after you got a “tie game”
After you played with 5 citizens, you can “isolate” yourself
All the players
Playing phase
Your micro:bit will show you an alphabet
Remember it but do not tell anyone else
Starting phase
Your micro:bit will tell who you were infected by
Try to trace back to see who is the “Patient Zero”
End phase

## Slide 63: Infection Game
Game Rules:
Healthy
Keep playing
Sick
Keep playing
Dead
Stop playing
(Contagious if infected)
(Contagious)
(Not contagious)

## Slide 64: Infection Game
The game and the code:
https://makecode.microbit.org/projects/infection
20000 ms = 20s
0s
40000 ms = 40s

## Slide 65: Conclusion
Now you can:
Write easy programs by using “makecode”
Assemble the sensors, electronic parts and micro:bit for science investigation
3. Sensor calibration
4. Add the TEAM elements to S (Biology)

## Slide 66
Jockey Club STEAM Education Resources Sharing Scheme 賽馬會STEAM教育資源共享計劃

## Slide 67: Jockey Club STEAM Education Resources Sharing Scheme
4 years project
Funded by The Hong Kong Jockey Club Charities Trust
Work together with secondary schools
Providing relevant support to secondary schools to implement STEAM education
Development of STEAM related materials
Student learning activities
Teachers’ professional development
An information hub for sharing good practices

## Slide 68: Useful Links
Enquiry:
Phone: 2768 6804
Email: steam@hkmu.edu.hk
Our website
List of Modules
List of Workshops