## Slide 1
Jockey Club STEAM Education Resources Sharing Scheme
First Edition Dec 2019
STEAM Activity and Experiment: Plane Launcher x Micro:bit

## Slide 2: Introduction
3. What is the most difficult part of designing a STEAM activity?
1. How many of you did this before?
2. What kinds of STEAM activity you want your students to participate in?

## Slide 3: Introduction
Experiment:
Variables
Time
Temp.
Angle
pH
Light
Rate
Speed
Turbidity

## Slide 4: Introduction
Variables
Time
Temp.
Angle
pH
Light
Rate
Speed
Turbidity
Tools
Measure
Experiment:

## Slide 5: Introduction
Variables
Tools
Measure
STEAM
Experiment:

## Slide 6: Introduction
After this workshop, you will be able to:
Write easy programs by using “makecode”
Make a Timing Gate
Make a Plane Launcher
Add the TEAM elements to Science

## Slide 7: Introduction
Programming: By using makecode/micro:bit
We are going to make:
  Timing gate
  Plane launcher
  All sensors and parts are safe, cheap, easy-to-use and compatible to micro:bit

## Slide 8: Introduction

## Slide 9: Introduction
I/O Pin
Input/output pin
In micro:bit:
“Read” = Input to micro:bit
“Write” = Output from micro:bit

## Slide 10: Coding
1. Bluetooth connection
Download the app “micro:bit”

## Slide 11: Coding
Click “Manage Connections”
Then “Pair a micro:bit”

## Slide 12: Coding
Reset
Press and release the “reset” button 3 times

## Slide 13: Coding
COPY the LED columns from you micro:bit
Enter the same pattern to the app

## Slide 14: Coding
1 and 0
1
0

## Slide 15: Timing Gate
Makecode website: makecode.microbit.org
1. Timing Gate
It is used to check the speed of a moving car
Speed =
We need to obtain these two figures

## Slide 16: Timing Gate
Speed =
Starting
point
End point
Travelling distance

## Slide 17: Timing Gate
Starting
point
Open circuit
Closed circuit
Detected by
the micro:bit
Pin 0

## Slide 18: Timing Gate
Open circuit
Closed circuit
Detected by
the micro:bit
End
point
Pin 1

## Slide 19: Timing Gate
Speed =
Starting
point
End
point
Travelling distance

## Slide 20: Coding
On pin P0 pressed
= when the P0 circuit was closed
Running time (ms)
= Activate timing
Record down that particular
time as “Initial time”
Makecode website: makecode.microbit.org
1. Timing Gate

## Slide 21: Coding
Record down that particular time
as “Final time”
Makecode website: makecode.microbit.org
1. Timing Gate

## Slide 22: Coding
Calculating the time needed
Converting from ms to s
Input the distance travelled
Calculating the speed in m/s
Math part:
Makecode website: makecode.microbit.org
1. Timing Gate

## Slide 23: Coding
Download the program
to micro:bit

## Slide 24: Timing Gate
Speed =
Starting
point
End
point
Travelling distance

## Slide 25: Plane Launcher
Makecode website: makecode.microbit.org
2. Plane Launcher

## Slide 26: Plane Launcher
Makecode website: makecode.microbit.org
2. Plane Launcher

## Slide 27
零件 Components:
1-3: 主體 Body
4: 平台 Platform
5-6: 平台遮板 Platform Plate
7-10: 摩打遮板 Motor Shield
11: 電綫遮板 Wire Shield
12: 手柄 Handle
13: 電池盒（可選）Battery Box (Optional)

## Slide 28
零件 Components:
9V 電池 Battery x1
摩打 Motor x2
電源摯 Power Button x1
電池插座 Battery Socket x1
電綫 Wires x2 (~15cm for each wire)
車轆 Wheels x2
條狀海綿 Sponge Strip x2
長木棍 Longer Sticks x2
短木棍 Shorter Sticks x2

## Slide 29
工具 Tools:
熱熔膠槍 Hot Glue Gun
剪綫鉗 Wire Chopper
鎅刀 Cutter
膠紙 Tape
(大會提供 不在圖中)
(Not in the picture, officially provided)

## Slide 30
從紙板上取下主體零件（1，2，3） Remove the body (1, 2, 3) from the cardboard

## Slide 31
把主體組裝好
Assemble the body

## Slide 32
從紙板上取下平台（4）
Remove the platform (4) from the cardboard

## Slide 33
把主體和平台組合起來
Assemble the body and the platform together
Long
Short

## Slide 34
從紙板上取下平台遮板（5，6）
Remove the platform plates (5, 6) from the cardboard

## Slide 35
將平台遮板貼合於平台上
Paste the platform plates onto the platform

## Slide 36
將兩條長木棍分別貼於中間空隙的兩邊
Paste the longer sticks into the gap separately

## Slide 37
從紙板上取下摩打遮板（7，8，9，10）
Remove the motor shields (7, 8, 9, 10) from the cardboard

## Slide 38
將摩打遮板粘合於主體與平台之間
Paste the motor shields onto the position between the body and the platform

## Slide 39
現在，發射器應該是這樣的
The launcher should look like this now

## Slide 40
將兩條電綫分別剪開兩等份，再各自連接到摩打上
Cut each wire into 2 equal sections, and connect them with the motors

## Slide 41
從紙板上取下電綫遮板（11）
Remove the wire shield (11) from the cardboard

## Slide 42
1. 使用熱熔膠固定摩打
Stabilize the motors with the hot glue
2. 將電池遮板粘合於發射器之下，摩打旁邊
Paste the wire shield next to the motors, at the bottom of the launcher
1
2

## Slide 43
將兩個摩打的正負極各自連接
Connect the +ve sides and -ve sides of the two motor
負-ve
正+ve

## Slide 44
將電池插座與摩打連接，形成一個完整的電路
Connect the battery socket with the motors to form a circuit

## Slide 45
請檢查摩打的轉向，它們必須以相反的方向轉動， 才能將紙飛機推出發射器
Please check the directions of the motors
They should spin in the opposite directions to push the plane forward

## Slide 46
用熱熔膠及膠紙固定電綫
Stabilize the wires with hot glue and tape

## Slide 47
將電池插座的紅色電綫的中間剪斷 Cut the red wire of the battery socket into half
把電源摯粘在發射器下 Paste the power button at the bottom of the launcher
1
2

## Slide 48
將紅色電綫的兩端連接到電源摯上 Connect two edges of the red line to the power button
用熱熔膠固定電綫和電源摯 Stabilize the wires and button with hot glue
IMPORTANT
1
2

## Slide 49
將其中一支短木棍粘在發射器尾端，以便放置電池
Paste a shorter stick at the end of the launcher, for the battery

## Slide 50
電池可以用膠紙固定
The battery should be installed with tape for stabilization

## Slide 51
從紙板上取下手柄（12）
Remove the handle (12) from the cardboard

## Slide 52
沿著虛綫摺叠出手柄，再噴上適量熱熔膠
Fold the handle with the dotted lines, and squeeze a suitable amount of hot glue into the gaps

## Slide 53
將手柄安裝至發射器上
Install the handle onto the launcher

## Slide 54
製作兩個海綿轉輪，以熱熔膠粘合
Make two wheels with sponge strips, with hot glue

## Slide 55
最後，安裝轉輪至發射器上
Finally, install wheels onto the motors

## Slide 56: Plane Launcher
“Rotation”
Pitch
Roll
Pitch
Roll
Makecode website: makecode.microbit.org
2. Plane Launcher with Micro:bit

## Slide 57: Plane Launcher
Makecode website: makecode.microbit.org
2. Plane Launcher with Micro:bit

## Slide 58: Plane Launcher
Set a desired launching angle e.g. 45o
The micro:bit will help you to check the angle
Once it is 45o, it will turn on the motors
Makecode website: makecode.microbit.org
2. Plane Launcher with Micro:bit

## Slide 59: Plane Launcher
Extension board
and a relay
Makecode website: makecode.microbit.org
2. Plane Launcher with Micro:bit

## Slide 60: Plane Launcher
Relay
NC = Normal Closed
NO = Normal Open
We use the micro:bit to control
the “switch”
Image source: StackExchange licensed under CC BY-SA 4.0.

## Slide 61: Coding
I/O Pin
Input/output pin
In micro:bit:
“Read” = Input to micro:bit
“Write” = Output from micro:bit
Makecode website: makecode.microbit.org
2. Plane Launcher with Micro:bit

## Slide 62: Coding
I/O Pin
1
0
Makecode website: makecode.microbit.org

## Slide 63: Coding
Makecode website: makecode.microbit.org
2. Plane Launcher with Micro:bit plus

## Slide 64: Plane Launcher
SIG to IN
3.3V to VCC
GND to GND
Makecode website: makecode.microbit.org
2. Plane Launcher with Micro:bit plus

## Slide 65: Plane Launcher
NC
NO
COM
From battery to motor
Connecting the
two motors
From motor
to relay
From Battery to relay

## Slide 66: Conclusion
Now you can:
Write easy programs by using “makecode”
Make a Timing Gate
Make a Plane Launcher
4. Add the TEAM elements to Science