## Slide 1
Jockey Club
STEAM Education Resources Sharing Scheme
Cal”U”Later

## Slide 2: Workshop Rundown 工作坊流程
Briefing on Safety and Experiment
簡介安全守則及實驗內容
Sample preparation of ICP-MS
實驗時間：準備樣本
Demonstration: Group 1: ICP-MS/ Group 2: FTIR-ATR
第一組：電感耦合電漿質譜儀示範/ 第二組：傅里葉轉換衰減全反射紅外光譜儀
Science tasting of FTIR-ATR
體驗 – 傅里葉轉換衰減全反射紅外光譜儀
Complete the worksheet
完成工作紙

## Slide 3: Inductively Coupled Plasma Mass Spectrometry (ICP-MS) 電感耦合電漿質譜儀
Objective 目的
Determine metal contents in mineralized water or beverage sample using Inductively Coupled Plasma Mass Spectrometry (ICP-MS) 使用電感耦合電漿質譜儀 (ICP-MS) 檢測礦泉水或飲料樣本中的金屬含量
  Zinc content in a Redoxon tablet
(一粒 Redoxon tablet 的鋅含量)

## Slide 4: Inductively Coupled Plasma Mass Spectrometry (ICP-MS) 電感耦合電漿質譜儀

## Slide 5: Mass Spectrometry (MS) 質譜儀
Produce, separate and detect ions in the gas phase

## Slide 6: Mass Spectrometry (MS) 質譜儀
Aspirin
Molecule
Ion
Anion of aspirin
What is the empirical formula of these two?
C9H8O4
C9H7O4

## Slide 7: Mass Spectrometry (MS) 質譜儀
What is the molecular weight of these two?
Image source: Image / Simon 03 / CC BY-SA 3.0

## Slide 8: Mass Spectrometry (MS) 質譜儀
Produce, separate and detect ions in the gas phase

## Slide 9: Operation of ICP-MS 電感耦合電漿質譜儀操作原理
The atoms are ionized and are then differentiated on the basis of their mass-to-charge ratio and a detector receives an ion signal proportional to the concentration 原子被離子化及偵測並根據其質荷比（質量-電荷比）進行排序的分析技術

## Slide 10: Fourier-Transformed Infrared - attenuated total reflection Spectroscopy (FTIR-ATR) 傅里葉轉換衰減全反射紅外光譜儀
Objective 目的
Testing of the textile by FTIR-ATR technique 使用FTIR-ATR技術分辨紡織物料

## Slide 11: Electromagnetic Spectrum 電磁波譜

## Slide 12: IR Spectrum 紅外光譜
Image / LibreText / CC BY-NC-SA 4.0

## Slide 13: IR Spectrum 紅外光譜

## Slide 14: Different Textile Materials 不同的紡織物料

## Slide 15: Testing the Textile Materials 紡織物料測試

## Slide 16
Frequency Range | Absorption (cm-1) | Appearance | Group | Compound Class | Comments
4000-3000 cm-1 | 3700-3584 | medium, sharp | O-H stretching | alcohol | free
 | 3550-3200 | strong, broad | O-H stretching | alcohol | Intermolecular bonded
 | 3500 | medium | N-H stretching | primary amine | 
 | 3400 |  |  |  | 
 | 3400-3300 | medium | N-H stretching | aliphatic primary amine | 
 | 3330-3250 |  |  |  | 
 | 3350-3310 | medium | N-H stretching | secondary amine | 
 | 3300-2500 | strong, broad | O-H stretching | carboxylic acid | usually centered on 3000 cm-1
 | 3200-2700 | weak, broad | O-H stretching | alcohol | intramolecular bonded
 | 3000-2800 | strong, broad | N-H stretching | amine salt | 
3000-2500 cm-1 |  |  |  |  | 
3000-2500 cm-1 | 3333-3267 | strong, sharp | C-H stretching | alkyne | 
 | 3100-3000 | medium | C-H stretching | alkene | 
 | 3000-2840 | medium | C-H stretching | alkane | 
 | 2830-2695 | medium | C-H stretching | aldehyde | doublet
 | 2600-2550 | weak | S-H stretching | thiol | 

## Slide 17
Frequency Range | Absorption (cm-1) | Appearance | Group | Compound Class | Comments
2400-2000 cm-1 |  |  |  |  | 
2400-2000 cm-1 | 2349 | strong | O=C=O stretching | carbon dioxide | 
 | 2275-2250 | strong, broad | N=C=O stretching | isocyanate | 
 | 2260-2222 | weak | C≡N stretching | nitrile | 
 | 2260-2190 | weak | C≡C stretching | alkyne | disubstituted
 | 2175-2140 | strong | S-C≡N stretching | thiocyanate | 
 | 2160-2120 | strong | N=N=N stretching | azide | 
 | 2150 |  | C=C=O stretching | ketene | 
 | 2145-2120 | strong | N=C=N stretching | carbodiimide | 
 | 2140-2100 | weak | C≡C stretching | alkyne | monosubstituted
 | 2140-1990 | strong | N=C=S stretching | isothiocyanate | 
 | 2000-1900 | medium | C=C=C stretching | allene | 
 | 2000 |  | C=C=N stretching | ketenimine | 

## Slide 18
2000-1650 cm-1 | 2000-1650 | weak | C-H bending | aromatic compound | overtone
 | 1870-1540 |  |  |  | 
 | 1818 | strong | C=O stretching | anhydride | 
 | 1750 |  |  |  | 
 | 1815-1785 | strong | C=O stretching | acid halide | 
 | 1800-1770 | strong | C=O stretching | conjugated acid halide | 
 | 1775 | strong | C=O stretching | conjugated anhydride | 
 | 1720 |  |  |  | 
 | 1770-1780 | strong | C=O stretching | vinyl / phenyl ester | 
 | 1760 | strong | C=O stretching | carboxylic acid | monomer
 | 1750-1735 | strong | C=O stretching | esters | 6-membered lactone
 | 1750-1735 | strong | C=O stretching | δ-lactone | γ: 1770
 | 1745 | strong | C=O stretching | cyclopentanone | 
 | 1740-1720 | strong | C=O stretching | aldehyde | 
 | 1730-1715 | strong | C=O stretching | α, β-unsaturated ester | or formates
 | 1725-1705 | strong | C=O stretching | aliphatic ketone | or cyclohexanone or cyclopentenone
 | 1720-1706 | strong | C=O stretching | carboxylic acid | dimer
 | 1710-1680 | strong | C=O stretching | conjugated acid | dimer
 | 1710-1685 | strong | C=O stretching | conjugated aldehyde | 
 | 1690 | strong | C=O stretching | primary amide | free (associated: 1650)
 | 1690-1640 | medium | C=N stretching | imine / oxime | 
 | 1685-1666 | strong | C=O stretching | conjugated ketone | 
 | 1680 | strong | C=O stretching | secondary amide | free (associated: 1640)
 | 1680 | strong | C=O stretching | tertiary amide | free (associated: 1630)
 | 1650 | strong | C=O stretching | δ-lactam | γ: 1750-1700 B: 1760-1730

## Slide 19
1670-1600 cm-1 | 1678-1668 | weak | C=C stretching | alkene | disubstituted (trans) | Disubstituted (trans) | 
 | 1675-1665 | weak | C=C stretching | alkene | trisubstituted | trisubstituted | 
 | 1675-1665 | weak | C=C stretching | alkene | tetrasubstituted | tetrasubstituted | 
 | 1662-1626 | medium | C=C stretching | alkene | disubstituted (cis) | disubstituted (cis) | 
 | 1658-1648 | medium | C=C stretching | alkene | vinylidene | vinylidene | 
 | 1650-1600 | medium | C=C stretching | conjugated alkene |  |  | 
 | 1650-1580 | medium | N-H bending | amine |  |  | 
 | 1650-1566 | medium | C=C stretching | cyclic alkene |  |  | 
 | 1648-1638 | strong | C=C stretching | alkene | monosubstituted | monosubstituted | 
 | 1620-1610 | strong | C=C stretching | α.β-unsaturated ketone |  |  | 
1600-1300 cm-1 |  |  |  |  |  |  | 
1600-1300 cm-1 | 1550-1500 | strong | N-O stretching | nitro compound |  |  | 
 | 1372-1290 |  |  |  |  |  | 
 | 1465 | medium | C-H bending | alkane | methylene group | methylene group | 
 | 1450 | medium | C-H bending | alkane | methyl group | methyl group | 
 | 1375 |  |  |  |  |  | 
 | 1390-1380 | medium | C-H bending | aldehyde |  |  | 
 | 1385-1380 | medium | C-H bending | alkane | gem dimethyl | gem dimethyl | 
 | 1370-1365 |  |  |  |  |  | 
1400-1000 cm-1 |  |  |  |  |  |  | 
1400-1000 cm-1 | 1440-1395 | medium | O-H bending | carboxylic acid |  |  | 
 | 1420-1330 | medium | O-H bending | alcohol |  |  | 
 | 1415-1380 | strong | S=0 stretching | sulfate |  |  | 
 | 1200-1185 |  |  |  |  |  | 
 | 1410-1380 | strong | S=O stretching | sulfonyl chloride |  |  | 
 | 1204-1177 |  |  |  |  |  | 
 | 1400-1000 | strong | C-F stretching | fluoro compound |  |  | 

## Slide 20: Sample Preparation

## Slide 21: Sample Preparation 準備樣本
Step 1 步驟1
Prepare Redoxon® pellets 準備維多C®
Step 2 步驟2
Break the Redoxon® tablet into 4 pieces and weigh the ¼ tablet using a 100 mL beaker 將維多C®溶片分4份，把¼份放進100毫升的燒杯內秤重

## Slide 22: Sample Preparation 準備樣本
Step 3 步驟3
Add 50 mL nitric acid (HNO3) solution (1%) to dissolve the Redoxon® pellet until no gas bubbles are observed.
把50毫升1%硝酸溶液加到燒杯內以溶解維多C®直至沒有氣泡釋出

## Slide 23: Sample Preparation 準備樣本
Step 4 步驟4
Transfer the orange solution into a 100mL volumetric flask and fill up to mark with 1% HNO3 and mix well 將橙色溶液轉移到100毫升容量瓶，加入1%硝酸溶液至瓶身刻度並加以混合

## Slide 24: Sample Preparation 準備樣本
Step 5 步驟5
Transfer 1mL of the orange colour solution to a 10mL volumetric flask and make it up to the mark with 1% HNO3 solution
把1毫升橙色溶液轉移到10毫升容量瓶，並加入1%硝酸溶液至瓶身刻度
1mL (from 100 mL V-flask) + 9mL of HNO3 solution = 10mL mixture 由100毫升的容量瓶取出1毫升加入9毫升硝酸溶液 = 10毫升溶液
Thus, the Redoxon® sample is diluted by 10 times
維多C®因此稀釋了10倍

## Slide 25: Sample Preparation 準備樣本
Step 6 步驟6
Transfer 2mL of the mineralized water to the 10mL volumetric flask and make up to the mark with 1% HNO3 solution.
把2毫升礦泉水轉移到10毫升容量瓶，並加入1%硝酸溶液至瓶身刻度
2mL (mineralized water) + 8mL of HNO3 solution = 10mL mixture
2毫升礦泉水 + 8毫升硝酸溶液 = 10毫升溶液
Thus, the mineralized water sample is diluted by 5 times
礦泉水因此稀釋了5倍

## Slide 26: Sample Preparation 準備樣本
Step 7 步驟7
For both samples, fill up the centrifuge tube (15mL) with 10mL diluted sample solution for heavy metal analysis using ICP-MS
根據所準備的樣本，將10毫升的溶液樣本加入於15毫升離心管中並進行重金屬測試

## Slide 27: Data Interpretation

## Slide 28: Data Interpretation
Hints:
How many gram of Redoxon tablet was used?
What was the dilution factor of the final testing solution?
How many mL of the final testing solution was used for the testing?
What is the weight of a Redoxon tablet?

## Slide 29: Data Interpretation
Hints:
What was the dilution factor of the final testing solution?
How many ml of the final testing solution was used for testing?
What was the total volume of a can of coke?

## Slide 30: Experimental Results

## Slide 31: IR Spectrum 紅外光譜

## Slide 32: Sample A: 樣本A：

## Slide 33: Sample B: 樣本B：

## Slide 34: Sample C: 樣本C：

## Slide 35: Results 實驗結果
Group | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Result (mg/L) |  |  |  |  |  |  |  |  |  |  | 

## Slide 36: Worksheet Answer 工作紙答案
From the measurement:
Its concentration was: X mg/L (ppm)
The 1 ml solution added:
Its concentration of was: 10X mg/L (ppm)
In the 100 ml solution:
The amount of zinc was: ?????????
The zinc content of a tablet: ?? mg

## Slide 37: Results 實驗結果
Let the zinc in ¼ tablet be mg
The conc. of it
= mg/100ml = mg/L
1 ml
The conc. of it
= mg/L (ppm)

## Slide 38: Results 實驗結果
How many grams of Zinc was in 1 tablet?
= mg / the weight of the ¼ tablet x 4.5g (the weight of the whole tablet)
Group | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Result (mg in 1 tablet) |  |  |  |  |  |  |  |  |  |  | 

## Slide 39: Worksheet Answer 工作紙答案
From the measurement:
Its concentration was: X mg/L (ppm)
The 1.25 ml coke sample added:
Its concentration w: 20X mg/L (ppm)
: 20/1000 X mg/ml
: 1/50 X mg/ml
The caffeine content of a can: 330 x 0.02X mg

## Slide 40: Thank you