## Slide 1
Biosafety and Biosecurity
Jockey Club
STEAM Education Resources Sharing Scheme

## Slide 2
Bio Hazard
Bio Security
Bio Safety

## Slide 3: Biosafety
Definition
  Centers for Diseases Control and Prevention (CDC); USA
  Biosafety is the use of safety precautions to decrease the potential risk of laboratorians in handling infectious microbe and minimize the contamination of the work environment and the community.
Adapted from cdc.gov

## Slide 4: Biosecurity
Definition
  World Health Organization (WHO)
  Biosecurity is a strategic and integrated approach to analysing and managing relevant risks to human, animal and plant life and health and associated risks for the environment.
  Recognition of the critical linkages between sectors and the potential for hazards to move within and between sectors, with system-wide consequences.
  Hence, the goal of biosecurity is to prevent, control and/or manage risks to life and health in particular biosecurity sector.
Adapted from who.int
Notes: https://www.youtube.com/watch?v=6aK2CKrdjbE

## Slide 5: Four main routes for microorganisms entering human body
Skin with wounds or cuts
Mucous membranes of eyes, nose or mouth
Respiratory route
Eating or drinking

## Slide 6: Standard Microbiological Practices
Applicable to all laboratories,
  Washing hands after working with infectious materials and before leaving the laboratory
  Routinely decontaminating work surfaces
    E.g. 70% ethanol or 10% chlorine bleach
  Not eating or drinking in laboratory
  Mouth pipetting is prohibited

## Slide 7: WHO Classification of Infectious Microorganisms by Risk Group
Risk Group 1
  No or low individual and community risk
  A microorganism that is unlikely to cause human or animal disease.
Risk Group 2
  Moderate individual risk, low community risk
  A pathogen that can cause human or animal disease but effective treatment and preventive measures are available.
Risk Group 3
  High individual risk, low community risk
  A pathogen that usually causes serious human or animal disease but effective treatment and preventive measures are available.
Risk Group 4
  High individual and community risk
  A pathogen that usually causes serious human or animal disease.
  Effective treatment and preventive measures are not usually available.

## Slide 8: Biosafety Level (BSL)
Four biosafety levels
Each level has specific measures for controlling microbes and biological agents.
  Laboratory practices
  Safety equipment
  Facility construction
Adapted from thebiologynotes.com
Adapted from cdc.gov

## Slide 9: Biosafety Level (BSL)
Factors for determining the levels of containment
  Infectivity
  Severity of disease
  Transmissibility, and
  Nature of the work conducted.
BSL-4
BSL-3
BSL-2
BSL-1
High Risk Microbes
Low Risk Microbes
Adapted from cdc.gov
Notes: https://www.youtube.com/watch?v=xNYASNEdgg8

## Slide 10
Agent
  No or low individual and community risk e.g. nonpathogenic strain of E. coli
Laboratory
  Basic teaching; research
Laboratory Practices
  Standard Microbiological Practices
Safety Requirement
  Open bench and sink required
Adapted from cdc.gov

## Slide 11: Standard Microbiological Practices
Applicable to all laboratories,
  Washing hands after working with infectious materials and before leaving the laboratory
  Routinely decontaminating work surfaces
    E.g. 70% ethanol or 10% chlorine bleach
  Not eating or drinking in laboratory
  Mouth pipetting is prohibited

## Slide 12: Personal Protective Equipment (PPE)
(Long Pants)
Shoes
Source: WikiHow licensed under CC BY-NC-SA 3.0

## Slide 13: Autoclave
The use of autoclaves in schools is governed by the Code of Practice for Owners of Boilers and Pressure Vessels, issued by the Labour Department
Sterilization:
  Steam under pressure (autoclave) at 121°C, 15 psi pressure for at least 30 minutes

## Slide 14
Agent
  Moderate individual risk; low community risk, e.g. Staphylococcus aureus
Laboratory
  Primary health services; diagnostic services; research
Laboratory Practices
  Level 1 plus limited access; biohazard sign; appropriate PPE
Safety Requirement
  Level 1 plus biological safety cabinet (BSC); autoclave
Adapted from cdc.gov
Notes: https://www.who.int/ihr/publications/biosafety-video-series/en/

## Slide 15: BSC

## Slide 16: BSL3
Agent
  High individual risk; low community risk e.g. Mycobacterium tuberculosis
Laboratory
  Special diagnostic services; research
Laboratory Practices
  Level 2 plus controlled access; special PPE with respirator
Notes: https://www.youtube.com/watch?v=z2Dka1VC2PE

## Slide 17
Safety Requirement
  Level 2 plus appropriate BSC;
  hands-free sink;
  directional airflow;
  2 sets of self-closing and locking doors
Adapted from cdc.gov

## Slide 18: HEPA Filter
High Efficiency Particulate Air (HEPA) filter
~ 0.3 μm

## Slide 19: BSL4
Agent
  High individual and community risk, e.g. Ebola
Laboratory
  Dangerous pathogen units
Laboratory Practices
  Level 3 plus full covered PPE with positive pressure,
  air-supplied;
  change clothing before entering;
  shower and decontaminate all materials before exiting
Notes: https://www.youtube.com/watch?v=xnNohYMkuAE

## Slide 20
Safety Requirement
  Level 3 plus isolated zone;
  Class III BSC;
  dedicated supply and exhaust air;
  vacuum and decontamination systems
Adapted from cdc.gov

## Slide 21: Question
COVID-19

## Slide 22: Suggested Solution
According to the biosafety guidelines in CDC,
  Routine Diagnostic Testing
     BSL-2 laboratory
  Environmental Specimen Testing
    BSL-2 laboratory with unidirectional airflow
    BSL class II
    BSL-3 precautions, including respiratory protection and a designated area for donning and doffing PPE
  Virus Isolation
    BSL-3 laboratory
      Antiviral research
      Vaccine development
      Virus stability research
      Pathogenesis research

## Slide 23: Risk assessment
Factors | Explanation
1. The type of microorganism to be studied and the suggested biosafety level | Estimate the risk level of microbial culture
2. Well-planned laboratory procedures | Minimize the potential risk
3. Volume of cultures | The greater the volume of liquid culture, the higher the risk
4. Composition of culture media | Possibility of culture of selective microbes
5. Incubation conditions | Possibility of culture of selective microbes
6. Laboratory faculties and equipment | Adequate for the experiment
7. Proper procedure of disposal | Minimize the contamination
8. Expertise of teachers and technicians | Capability of conducting the experiment
9. Study level of the students | Capability of the level of experiment

## Slide 24: Safe organisms commonly used
Species | Risk Group
E.Coli K-12 and derivative (DH5alpha, TOP10, etc.) | 1
S. Cerevisiae | 1
Most human and mammal cell lines | 2
Lactobacillus spp. | 1
Bacillus subtills | 1

## Slide 25: Aseptic techniques in Microbiology and Biotechnology
Flame tube
Transfer from broth to plate/ broth
Flame tube
Cap & put back in rack

## Slide 28
Check out the regulations and images on this page to understand more about Lab Safety
Safety/Working Safely - 2019.igem.org