## Slide 1
Jockey Club
STEAM Education Resources Sharing Scheme
Message From
Your Heart

## Slide 2: Rundown (流程)
Heart anatomy and circulation
Cardiac conduction system
Heart rate detection
Electrocardiogram
Activity: Micro:bit X ECG device

## Slide 3: Find your heart (找出您的心臟)
Put your hand on your heart. Can you feel it beating?
Located in the middle of your chest
Towards the left side (commonly) of your body
Under your lungs
Protected by your rib cage
Weight: 250-350 g
about a can of Coke
Image / Bryan Brandenburg / CC BY-SA 3.0

## Slide 4: Dextrocardia (右位心)
Birth defect
Approximately 1 in every 12,000 births
Not a hereditary disease
During embryonic development, the heart initially locates on the right side of the body and slowly moves to the left side.
The result of a failure in normal positioning

## Slide 5: Cardiovascular system (心血管系統) and Circulation (循環)
Cardiovascular system = heart + blood vessels (arteries, veins, and capillaries) + blood
Circulation = pulmonary circulation (between lung and heart) + systemic circulation (between heart and the rest of body)
Circulation system / NetJapa / CC BY-NC 4.0

## Slide 6: Heart Anatomy (心臟解剖學)
(bicuspid valve / left atrioventricular valve)
(pulmonic / right semilunar valve)
(left semilunar valve)
(right atrioventricular valve)

## Slide 7: Cardiac cycle (心跳週期)
Diastole (filling)
Systole (pumping)
Aorta
Pulmonary veins
Right atrium
Right ventricle
Pulmonary veins
Vena cava
Pulmonary arteries
Left atrium
Left
ventricle
Figure 1 / OpenStax / CC BY 4.0
VIDEO

## Slide 8: Can we control our heartbeat? 我們能控制自己的心跳嗎？
Involuntary muscle
Autonomic nervous system (自主神經系統)
NO!
不受意志支配
WHY?
意志
思考
決定
行動

## Slide 9: Then how the heart regulates its rhythm?

## Slide 10: Cardiac Conduction System (心臟傳導系統)
Sinoatrial (SA) node 60-100/min
Atrioventricular (AV) node 40-60/min
Bundle of His <20/min (ventricular septum)
Purkinje fibers <20/min (ventricular wall)
Anatomy & Physiology / SBCCOE / CC BY SA 4.0
Ventricular wall
Ventricular septum
Bundle of His

## Slide 11: How can we determine whether our heart is healthy or not?

## Slide 12: Activity 1: Detecting Heart Rate
Place two fingers on your wrist, just below the base of your thumb.
If it is difficult to detect your heart rate at your wrist, you can also check the side of your neck.
Count your pulse for 15 seconds and then multiply the number by 4.
resting pulse rate: 60-100/min

## Slide 13
Heart rate is a non-specific indicator of health conditions. How can we specifically monitor the health of our heart?
Tachycardia | Bradycardia
Heart rate >100/min normal: during exercise, excitement, or pregnancy Abnormal: low potassium levels, an overactive thyroid gland, fever, heart disease, and more | Heart rate < 60/min Normal: athletes Abnormal: high potassium levels, an overactive thyroid gland, heart disease, medications, and more

## Slide 14: Electrocardiogram, ECG (心電圖)
ECG of PVC / medipics1066 / CC BY 2.0

## Slide 15: Electrocardiogram, ECG (心電圖)
Detects electrical signals from the heart
Captures the electrical activity of every heart motion
Presents it in repetitive waveforms
Graph: Voltage vs time
Voltage
Time
Anatomy & Physiology / SBCCOE / CC BY SA 4.0
Ventricular wall
Ventricular septum
Bundle of His

## Slide 16: Normal ECG waveform (正常心電圖波形)
Bundle of His
SA node
AV node
Purkinje fibres
P wave (1)
Atrial depolarization, contracting atria
QRS complex (3)
Ventricular depolarization, contracting ventricles
T wave (5)
Atrial repolarization, relaxing atria

## Slide 17: Diseases that can be identified from an ECG (可以從心電圖檢測出的疾病)
MI / Blausen Medical Communications, Inc. / CC BY 3.0
Pericarditis (心包膜炎)
Myocardial ischemia (心肌缺氧)

## Slide 18: Activity 2: Micro:bit as ECG Apparatus
+
Heart rate
Micro:bit

## Slide 19: Materials (材料)
1pc Micro:bit
1pc Extension board
1pc ECG chip
1pc USB connect
1pc “3-colors” electrode
5pcs wires
3pcs electrode pads

## Slide 20: Assemble (組裝)
Insert a Micro:bit into the expansion board.

## Slide 21: Assemble (組裝)
Connect the ECG chip to the expansion board as follows.
Extension board | ECG chip
G (column 1, black) | GND
V (column 1, red) | 3.3V
Pin 1 (column 1, yellow) | output
Pin 5 (column 5, yellow) | LO-
Pin 6 (column 6, yellow) | LO+
Pin 1
V
G
Pin 5
Pin 6
GND 3.3V
Output
LO-
LO+

## Slide 22: Assemble (組裝)
Connect the "3-colors" electrode to the ECG chip.

## Slide 23: Assemble (組裝)
Connect each colored electrode pad to its respective electrode.

## Slide 24: Assemble (組裝)
Connect the Micro:bit to a computer.
Done!
Now let's move on to coding.
😈

## Slide 25: Coding (編碼)
Go to MakeCode and build the following blocks.
Then, download the script to your Micro:bit!

## Slide 26: ECG detection (心電圖檢測)
Connect the electrodes to your body as shown in the figure.
Press button A to start measuring until a ✔ is displayed.
Right
Left
Image / Zorkun / CC BY-SA 3.0

## Slide 27: Find out your data (查找您的數據)
Go to the "MICROBIT" drive on your desktop.
Open "MY_DATA.HTM".
Download your data.

## Slide 28: Calculate heart rate (計算心率)
Plot a graph of voltage (output) versus time.
Calculate the heart rate by counting the number of R-peaks.

## Slide 29: Discussion (討論)
Can you identify standard ECG waveforms?
Is the heart rate measured using the Micro:bit the same as that measured at the wrist?
You can also exercise and then measure your heart rate again to observe changes in your heart rate.

## Slide 30: Summary (總結)
Heart anatomy and circulation
Cardiac conduction system
Heart rate detection
Electrocardiogram (ECG)
Activity: Micro:bit X ECG device

## Slide 31: Thank You