## Slide 1
Locating in
Darkness
Jockey Club
STEAM Education Resources Sharing Scheme

## Slide 2: Rundown
2.
3.
Characteristics of sound wave
4.
Speed of sound
5.
The principle of sonar and echolocation
6.
Making a ultrasonic distance sensor
Introduction to sound
7.
Discussion & Conclusion
1.
Visual impairment

## Slide 3: Visual impairment – Definition
Visual impairment (視障) is a range of conditions that
affect a person's ability to see
Includes partial sight and blindness (失明), can
affect one or both eyes
Can be caused by various factors
Can affect people of all ages
Have a significant impact (重大影響) on a person‘s
quality of life (生活質素), including their education,
employment, and social interactions
Photo by CDC on Unsplash

## Slide 4: Visual impairment – Data
Number of people with visual impairment:
  Hong Kong - 199,600 (~2.7%)
  Worldwide - Blind: 43 million (~0.5%)
- Moderate-to-severe (中度至重度) visual impairment: 295 million (~3.7%)

## Slide 5: Visual impairment – Aid
Visual impairment results in the dependency on other senses (依賴其他感官) (hearing, touch, smell, taste)
Devices can be created to help people with visual impairment to utilize (利用) these senses

## Slide 6: Introduction to sound
Sound is a form of wave.
A sound wave consists of vibrating particles (振動粒子).
The vibration propagates as an acoustic wave (聲波) through a transmission medium (傳輸介質), such as air (Sound cannot transmit through vacuum (真空!).

## Slide 7: Characteristic of sound – loudness
The loudness (響度) of sound
  The loudness of sound is measured as the sound intensity level (聲強級)
Sound intensity level
  Unit: decibel (dB) (分貝)

## Slide 8: Characteristic of sound – loudness
Typical sound intensity level:
Image / OpenStax / CC BY 4.0
Threshold of hearing (聽覺閾)
Normal conversation (日常對話)
Threshold of pain (痛閾)

## Slide 9: Characteristic of sound – pitch
The pitch (音高/音調) of a sound
  A sound with higher pitch (高音調) means the sound wave has higher frequency (高頻率)
The frequency of a sound wave
  Unit: Hertz (Hz) (赫茲/赫)
  Frequencies of common musical notes (音符):
    Middle C: 261.63 Hz
    A4 musical note: 440 Hz
  Human hearing frequency (人類聽覺頻率): 20 Hz ~ 20,000 Hz

## Slide 10: Test your hearing frequency
Listen to the YouTube audio, identify your own hearing frequency range

## Slide 11: Ultrasound
Normal hearing frequency of human: 20 Hz ~ 20,000 Hz
Sounds with frequencies greater than 20,000 Hz are called ultrasounds (超聲波)
is widely used in distance detection devices (測距裝置)
Infrasound
Audible frequencies
Ultrasound
20 Hz
20 KHz
2 MHz
200 MHz

## Slide 12: The speed of sound – Think about it…
Does a louder sound travel faster?
Does a sound with higher pitch travel faster?

## Slide 13: The speed of sound
A sound wave travels in air at a constant speed (恆速率) in fixed pressure and temperature (固定氣壓和溫度).
At 20°C, the speed of sound in air = 343 metres per second
It is not affected by the loudness or the pitch.

## Slide 14: What is echolocation (迴聲定位)?
Used by some animals in nature (such as bats).
Animals emit calls (呼叫) out to the environment and listen to the echoes (回聲) of those calls.
They use those echoes to locate and identify objects.

## Slide 15: Sonar (聲納)
SOund NAvigation and Ranging
Active sonar (主動聲納):
  Device emits a pulse (脈衝) of sound
  The pulse reaches an object and then reflects (反射) backwards
  The reflected pulse (or echo) is listened by the device

## Slide 16: The ultrasonic Sensor – HC-SR04
The transmitter (發射器) –
Emits ultrasonic signal
The receiver (接收器) –
Receives ultrasonic signal

## Slide 17: How does the ultrasonic sensor work?
The transmitter emits a sound signal (訊號).
The signal reaches the object and reflect backwards.
The receiver receives the signal after a certain time.

## Slide 18: How does the ultrasonic sensor work?
The sound wave travels a distance of 2d (in metre) in time t (in second).
Total Distance (總距離) = Speed (速率) × Time (時間)
2d = 343 × t
d = 171.5t

## Slide 19: Connection
Micro:bit |  | HC-SR04
Pin3 | 3.3V | Vcc
Pin0 | SIG | Trig
Pin8 | SIG | Echo
Pin9 | GND | Gnd

## Slide 20: Connection
Connect the micro:bit to an iPad or computer using a USB-MicroUSB wire

## Slide 21: Connection
Go to website https://makecode.microbit.org.
Under “My Projects”, click “New Project”.
Name your project according to your preference.

## Slide 22: Connection

## Slide 23: Coding

## Slide 24: Coding
P0: the ultrasound signal emitter
At t = 2 ms, the device starts emitting ultrasound
At t = 10 ms, the device stops emitting ultrasound
1 ms = 10-6 s

## Slide 25: Coding
P8: the ultrasound signal receiver
It records the time receiving the pulse as “time” (in ms)
Remark: 1 second = 1,000,000 ms

## Slide 26: Coding
d (in metre) = 171.5t (in second)
d (in cm) = d (in metre) x 100
= 17150t (in second)
= 17150 x time ÷ 1,000,000
≈ time ÷ 58

## Slide 27: Coding
Repeats the above instructions every 0.5 seconds (500 ms)

## Slide 28: Downloading the code

## Slide 29: Testing
Place an object near the sensor.
The micro:bit should display the corresponding distance.
There may be an error (誤差) of ±1 cm due to the rounding issue.

## Slide 30: Alert system (警報系統)
The sensor can detect the distance between an object and its location right now.
But it is unable to alert us when objects are near.

## Slide 31: The alert system
Our next step is to set the response (反應) of micro:bit according to different distances.

## Slide 32: The alert system
Micro:bit can emit sound.
When objects are near (distance ≤ 50 cm): The micro:bit emits sound more rapidly (快速地發聲) (the tempo (拍子) of the alert sound increases).
Otherwise (distance > 50 cm): The micro:bit emits sound less rapidly (慢速地發聲) (the tempo of the alert sound decreases).

## Slide 33: Coding – The alert system
Right click the “show number distance” code, and click “Delete”
Change the pause (ms) to 2000

## Slide 34: Coding – Tempo-varying alert

## Slide 35: Coding – Tempo-varying alert
On start, mute (靜音) the micro:bit
Set tempo to 240 bpm (beats per minute)

## Slide 36: Coding – Tempo-varying alert
1. Alert if “distance” is not a valid value.
2. If the distance value is not greater than 50 cm (close to us), the “pause” between two tones is short.
3. Otherwise, the “pause” is long.

## Slide 37: Coding – Tempo-varying alert
Press “A” to unmute.
Press “B” to mute.

## Slide 38: Blind experience
Cover your eye with a blindfold.
Try to navigate through the maze with a cane.

## Slide 39: Designing a hand-free navigator
Materials:
  Ultrasound distance sensor
  Battery box & batteries
  Electric wire
  Blindfold
Tools:
  Adverse tape
  Wire stripper
  Scissors
  Rubber bands

## Slide 40: Designing a hand-free navigator
Principles:
  Place the ultrasound module on your forehead.
  Install the sound-emitting component near the ear.
  Install the battery box at ease.

## Slide 41: The blindfolded game – rules
Each group selects a representative participant to wear a blindfold.
Participants are guided to the starting line and given a marker pen.
The distance sensor with alert system is switched on.
Based on the alert from the distance sensor, participants are required to reach the blackboard and draw a heart on the blackboard with the marker.
The fastest participant wins.
If a participant touches the blackboard with his/her body, he/she is disqualified.

## Slide 42: Modifications of the alert system
Modification 1: Change the type of indicator
  Change the tempo of the alert sound (current version)
  Change the volume of the alert sound
  Change the pitch of the alert sound
Modification 2: Increase the detecting intervals
  Our system only identifies “near (50 cm or less)” and “not near”.
  We can set up more logical comparison, such as: “very near (less than 20 cm)”, “near (20 cm to 50 cm)” and “not near”.

## Slide 43: Discussion
Question: How do we know that the speed of sound wave is not affected by the loudness or the pitch ?
Answer: Otherwise, we will hear a loud voice before a quiet voice, and a higher pitch note before a lower pitch note.

## Slide 44: Discussion
Question: Why do we use ultrasound instead of sound of normal audible frequencies?
Answer: We can use the device quietly.

## Slide 45: Discussion
Question: What challenges (挑戰) do you think people with sight impairments may face in their daily life?
Challenges with navigation (導航) and orientation (定向) in unfamiliar environments (不熟悉的環境)
Difficulties with identifying (識別) and using everyday objects and technology
A lack of accessibility (可達性) in public spaces and transportation
A higher risk of falls and injuries due to environmental hazards (環境危害) and obstacles (障礙物)
Dependence on others (依賴他人) for assistance with daily tasks

## Slide 46: Discussion
Question: Do you think the hand-free navigator is better than the cane?
Answer: (open-ended)

## Slide 47: Modern technologies related to ultrasound
Parking sensor of vehicle https://www.murata.com/en-global/products/sensor/ultrasonic/overview/apps
Thickness gauge https://cygnus-instruments.com/ultrasonic-thickness-gauge/
Medical diagnosis https://my.clevelandclinic.org/health/diagnostics/4995-ultrasound

## Slide 48: Thank you