## Slide 1: The Myth of RAT for COVID-19 新冠快測的迷思

## Slide 3: The Myth of RAT for COVID-19
COVID-19
Sample collection and result interpretation
3
4
RAT vs Rt-PCR
2
5
What is RAT?
1
6
Vaccination and SARS-CoV-2 Testing
How to select a suitable RAT?
RAT uses on other sample types

## Slide 4: What is RAT?
1

## Slide 5: What is COVID-19?
Coronaviruses
Cause illness ranging from the common cold to more severe diseases such as MERS and SARS-CoV.
SARS-CoV-2 was discovered in December 2019
Millions of confirmed human infections worldwide

## Slide 6: SARS-CoV-2 Testing
Nucleic Acid Amplification Tests (NAATs)
  Reverse Transcription – Polymerase Chain Reaction
Antigen Tests
Antibody Tests
Chest X-ray
Chest CT Scan
At-home Testing (Self-testing)
 Rapid Antigen Tests
Hospital / Laboratory

## Slide 7: What is RAT?
Rapid Antigen Test
Point of care testing device
Lateral flow technology
Antigen Test (viral proteins)

## Slide 8: Lateral Flow Technology

## Slide 9: Lateral Flow Technology

## Slide 10: Lateral Flow Technology

## Slide 11: Lateral Flow Technology

## Slide 12: RAT vs Rt-PCR
VS
2

## Slide 13: Testing Scenarios
person has signs or symptoms consistent with COVID-19
persons is asymptomatic, but has recent known or suspected close contact exposure to SARS-CoV-2.
Screening tests - Public health surveillance

## Slide 14: Rt-PCR (Reverse transcription-PCR)
detecting the presence of specific genetic material in virus
COVID-19 contains RNA
convert the RNA to DNA
Measure number of copies RNA (viral load)
Ct value = viral load
Notes: Pros
Minimally invasive – performed using nasal swabs, throat swabs and tests of saliva or other bodily fluids
Allows for social distancing – while some molecular tests, including RT-PCR, are sometimes conducted at a hospital or clinic, swabs can also be taken from the patient’s car or at home
Fewer false negatives in some instances – deep nasal swabs will have fewer false negatives compared with other tests, such as throat swabs or saliva tests
Cons
Long turnaround times – in some instances, RT-PCR tests can yield results in the same day or within one to two days, but test results taking up to one to two weeks have been reported during the pandemic
False negatives – molecular tests have been shown to produce results that say the patient doesn’t have the virus when they actually do; the rates of false-positives have ranged from 2% to 37%
Uncomfortable for some people – deep nasal swabs can be uncomfortable for some people, especially small children

## Slide 15: Rt-PCR (Reverse transcription-PCR)
Pros
Minimally invasive
Fewer false negatives in some instances
Cons
Long turnaround times
Uncomfortable for some people
Notes: Pros
Minimally invasive – performed using nasal swabs, throat swabs and tests of saliva or other bodily fluids
Allows for social distancing – while some molecular tests, including RT-PCR, are sometimes conducted at a hospital or clinic, swabs can also be taken from the patient’s car or at home
Fewer false negatives in some instances – deep nasal swabs will have fewer false negatives compared with other tests, such as throat swabs or saliva tests
Cons
Long turnaround times – in some instances, RT-PCR tests can yield results in the same day or within one to two days, but test results taking up to one to two weeks have been reported during the pandemic
False negatives – molecular tests have been shown to produce results that say the patient doesn’t have the virus when they actually do; the rates of false-positives have ranged from 2% to 37%
Uncomfortable for some people – deep nasal swabs can be uncomfortable for some people, especially small children

## Slide 16: Antigen Tests
Pros
Rapid results
Perform at home
Cons
High false-negative rate
Notes: Pros
Rapid results: The test uses technology similar to that used in a pregnancy test and yields results within minutes
Cons
Performed at a hospital or clinic: At-home antigen tests are not widely available, so patients typically have to travel to a hospital or clinic to have this test performed
High false-negative rate: Antigen tests produce higher false-negative rates than molecular RT-PCR tests, with some evidence suggesting rates as high as 50%

## Slide 17: RAT vs Rt-PCR
Sensitivity ?  Accuracy ?
> 80% (WHO)
Sensitivity = Detection power
Viral load

## Slide 18: Sensitivity

## Slide 19: RAT
Sensitivity affected by Viral load (Ct value)
Viral load Sensitivity
Viral load Sensitivity

## Slide 20: Specificity

## Slide 21: Sample Collection
3

## Slide 22: Sample Types
Nasopharyngeal Swabs
Nasal Mid-turbinate Swabs (Deep Nasal Swabs)
Anterior Nares Specimen Collection
Saliva

## Slide 23: Nasal Mid-turbinate Swabs
Nasopharyngeal Swabs

## Slide 24: Anterior nares specimen collection procedure
Wash hands before the procedure.
Tilt the head back to improve access the anterior nostril.
Press against the exterior naris by your finger.
Rotate the swab for 10 seconds, against the pressure of your finger (clockwise or counter clockwise).
Remove the swab from the first naris and repeat on the oppositive naris.
With your finger, gently press the side of the nose against the swab, as you rotate the swab with the other hand
Entire bulb is inside nose –
DO BOTH NOSTRILS

## Slide 25: Testing Procedure
Check the expiry date printed on expikit (Don’t use the red kit)
Make sure the kit is in room temperature (If not, wait for 30 mins before preforming the assay)
Get ready the extraction buffer solution (some kits require pre-mix the buffer before use)
Wash your hands with alcohol gel
Carefully collect your sample using the swab provided by the kit
Put the swab into the extraction buffer
Roll the swab 3-5 times

## Slide 26: Testing Procedure

## Slide 27
Check the expiry date printed on kit (Don’t use the expired kit)
Make sure the kit is in room temperature (If not, wait for 30 mins before preforming the assay)
Get ready the extraction buffer solution (some kits require pre-mix the buffer before use)
Wash your hands with alcohol gel
Carefully collect your sample using the swab provided by the kit
Put the swab into the extraction buffer
Roll the swab 3-5 times
Leave the swab in the extraction buffer for 1 min

## Slide 28
Dispose the swab into the biohazard waste bag
Add 3-4 drops (kit specific) into the sample well
Read the result after 15-20 minutes
Don’t read the results after 20 minutes (false positive result)

## Slide 29: Common mistakes
Not checking expiry date of the kit
Not washing your hands
Not proper collect the sample
Add too less or more extraction to the sample well
Wait too long to read the result

## Slide 30: When is the best time for doing the test?
Performs better in patients with high viral loads during the pre-symptomatic (1-3 days before symptom onset) and early symptomatic phases of the illness (within the first 5-7 days )
The chance of having false negative result will be higher 5-7 days after the onset of symptoms.

## Slide 31: Results Interpretation
4

## Slide 32
Hong Kong government recognizes positive results of rapid antigen test as confirmed cases since 25 Feb.
True positives are not required to be re-Tested

## Slide 33: What to do if test result is Negative?
Limitations (sensitivity)
Negative result of RAT should not be fully trusted
A single negative RAT result cannot preclude the possibility that the testee has been infected
During the period of incubation, or at an early stage of infection.

## Slide 34: What to do if test result is Invalid?
Check whether the sample type, sample collection method and testing method are correct.
Repeat the test with a new device.

## Slide 35: How to Prevent Invalid Results?
Correct sampling procedures
Follow the testing procedures
Store the kit at room temperature
Read the result within the time limit
Check the expiry date

## Slide 36: How to Dispose of the Materials after the Test?
Respiratory specimen is a kind of body fluid and is potentially infectious
Wrap and seal all the product components of the testing kit.
Dispose properly according to manufacturers’ instructions.
Wash hands properly afterwards.

## Slide 38: Could Vaccination Cause me to Test Positive for Covid-19?
5

## Slide 39: Vaccination and SARS-CoV-2 Testing
mRNA-based vaccines (Pfizer/BioNTech)
  small region of the viral genome = Spike protein
  not consist of the entire genome of the SARS-CoV-2 virus.
Inactivated virus COVID-19 vaccine (Sinovac)
Vaccination are not expressed in the respiratory (i.e., nasal) tract, which is sampled for Covid-19 PCR or antigen testing

## Slide 40: Can RAT Tests Work on Other Samples?
6

## Slide 43: Possible reasons
antigen + antibody ⇄ antigen - antibody complex
pH affect antigen-antibody reaction
Cross reactivity – interference
Not recommended on other types of samples

## Slide 44: How to Choose a Suitable RAT?
7

## Slide 45: Tips
The minimum sensitivity of 80% and specificity of 97%. (WHO)
Purchase from reputable suppliers.
Select the latest manufacturing date
Don’t just look at the prices
Read the product information carefully and understand the type of sample and method of collection
Recognized by the relevant authorities. E.g. Department of Health, National Medical Products Administration, European Union or U.S. Food and Drug Administration

## Slide 46: Important Points
Follow the instructions
Sample collection is one of the critical factors affecting the performance.
The performance of the RAT was affected by various factors, including viral load of the user and the prevalence of the disease.
RAT cannot replace the results of clinical interpretation and other laboratory tests, such as nucleic acid test.
Diagnosis of COVID-19 should be made by healthcare professionals only.

## Slide 47: New Medical Laboratory Science Programme in HKMU

## Slide 48: New Medical Laboratory Science Programme
Full-time, face-to-face
Four-year Bachelor’s Degree Programme
Laboratory-based
Clinical Practicum on Years 2 and 3

## Slide 49
Laboratory Facilities and Equipment

## Slide 50
Laboratories

## Slide 51: Career Prospect
HKMU will apply for programme accreditation.
Graduates of the proposed programme will be eligible to register as MLT (Part II)
Associate Medical Technologist (AMT) HK$ 28,780 - $48,860 (Point 13 - 24)
Medical Technologist HK$ 51,095 - $73,775 (Point 25 - 33)
Senior Medical Technologist HK$ 74,515 - $ 89,845 (Point 34 - 39)

## Slide 52: The programme will be launched in 2023

## Slide 53: Reference
Department of Health https://www.mdd.gov.hk/en/whats-new/rapid-antigen-tests-covid-19/index.html
Centres for Disease Control and Prevention https://www.cdc.gov/coronavirus/2019-ncov/symptoms-testing/testing.html